## Slide 1: Chapter 5 Large and Fast: Exploiting Memory Hierarchy

## Slide 2: 5.1 Introduction
SRAM:
  value is stored on a pair of inverting gates
  very fast but takes up more space than DRAM
  (4 to 6 transistors)
附录也无此内容

## Slide 3: Memories: Review
Word Line
Bit Line
C
Sense Amp
. . .
DRAM:
  value is stored as a charge on capacitor (must be refreshed)
  very small but slower than SRAM (factor of 5 to 10)
Write
  Charge bitline HIGH or LOW and set wordline HIGH
Read
  Bit line is precharged to a voltage halfway between HIGH and LOW, and then the word line is set HIGH(晶体管基集为高时，
  集电极与发射极导通).
  Depending on the charge in the capacitor, the precharged bitline is pulled slightly higher or lower.
  Sense Amplifier Detects change

## Slide 4: DRAM logical organization (256 Mbit) 1位数据读出
Column mutiplexer
Sense
Amps & I/O
Memory
Array
(16,384×16,384)
A0…A1
3
14
Data in
D
Q
Word Line
Storage
Cell
Data out
Row Decoder
…
Bit Line
14
14bit col. Addr. Reg.
14bit row addr Reg
16384 bit col. data Reg.
CAS（列选通）
RAS（行选通）
RAS: Row Access Strobe, CAS: Column Access Strobe

## Slide 5: DRAM logical organization (256 Mbit) 1位数据写入
上图未画出：有一个列解码器（14输入），列解码器有16384根输出线，每个输出线用于16384个三态门的控制线，这16384个三态门的输入连在一起，作为bit line的1位输入数据，这16384个三态门的输出作为memory array的列输入（其中1根为高或低，其余为高阻态）。
Column decoder
16384个3态门
Memory
Array
(16,384×16,384)
A0…A1
3
14
Data in
D
Q
Word Line
Storage
Cell
Data out
Row Decoder
…
Bit Line
14
14bit col. Addr. Reg.
14bit row addr Reg
16384 根3态门的控制线
CAS（列选通）
RAS（行选通）
control
input
output

## Slide 6: Problems in memory designing
In fact
Users want large and fast memories!
Memory technology | Typical access time | Cost per GByte (2004)
SRAM | 5ns | $4000-$10,000
DRAM | 50-70ns | $100-$200
Magnetic disk | 5,000,000-20,000,000ns | 

## Slide 7: Locality---- two important concepts
1. temporal locality (locality in time):
  If an item is referenced, it will tend to be referenced again soon.
2. spatial locality (locality in space):
  If an item is referenced, items whose addresses are close by will tend to be referenced soon.
As we know, these principles actually exists in most programs.
  Why does code have locality?
Our initial focus: two levels (upper, lower)
  block: minimum unit of data (block) for transfers
  hit: data requested is in the upper level
  miss: data requested is not in the upper level

## Slide 8: Solutions
Build a memory hierarchy
M
e
m
o
r
y
C
P
U
M
e
m
o
r
y
S
i
z
e
C
o
s
t
(
$
/
b
i
t
)
S
p
e
e
d
S
m
a
l
l
e
s
t
B
i
g
g
e
s
t
H
i
g
h
e
s
t
L
o
w
e
s
t
F
a
s
t
e
s
t
S
l
o
w
e
s
t
M
e
m
o
r
y
processor
Data are transferred
upper
Block (aka line): unit of copying between memory and cache
  May be multiple words

## Slide 9: Some important concepts
Hit: The CPU accesses the upper level and succeeds.
Miss: The CPU accesses the upper level and fails.
Hit time:
  The time to access the upper level of the memory hierarchy, which includes the time needed to determine whether the access is a hit or a miss.
miss penalty:
  The time to replace a block in the upper level with the corresponding block from the lower level
  发生缺失时，执行一条指令的时间=hit_time + miss_penalty

## Slide 10: Exploiting Memory Hierarchy
The method
  Hierarchies bases on memories of different speeds and size
  The more closely CPU the level is,the faster the one is.
  The more closely CPU the level is,the smaller the one is.
  The more closely CPU the level is,the more expensive
Levels in the memory hierarchy
Increasing distance from the CPU in access time
Size of the memory at each level

## Slide 11
Disk is normally the bottom of the hierarchy
Some systems use tape or file server in LAN as the next level below disk.
Design goal:
  the processor has an access time of level 1 of the hierarchy
  the processor has a memory as large as level n.

## Slide 12: There has been exploited Memory Hierarchy
The basics of Cache: SRAM and DRAM (main memory)
  The solution is in speed
Virtual Memory: DRAM and DISK
  The solution is in size

## Slide 13: 5.2 Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk
§5.2 Memory Technologies

## Slide 14: DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge, The charge can be kept for several milliseconds.
  Must periodically be refreshed
    This consumes 1% to 2% of the active cycles of the DRAM
    Performed on a DRAM “row”: refreshing an entire row (which shares a word line) with a read cycle followed immediately by a write cycle.

## Slide 15
下图1条DRAM内存条有8片chip（市场上也有9片或4片的）。
例子：1个chip内有4个bank，每个bank内有8个array（8个array决定了位宽是8bit），一个特定地址的数据只在其中1个bank中，1个bank的容量是64K*8bit（256 row * 256 column * 8bit），则这个chip有256k*8bit，位宽8bit。
  Chip的位宽由array数量决定，无关bank数量，增加chip内的bank数只会增加容量，不增加位宽。
  输入地址时，地址译码电路会选择其中的一个bank
  读数据的bank内地址是0xA1B4，clk1输入row-addr=0xA1,每个array读出1个row的256位存到row buffer（256 bits latches），8个array同时读出同1个row的256*8位存到row buffer， 接着clk2输入col-addr=0xB4, 会读出row buffer 内column-addr是0xB4处的8bit（对应bank内地址0xA1B4 ），row-addr不变 ，clk3和clk4输入col-addr=0xB5,0xB6, 依次读出0xA1B5处的8bit， 0xA1B6处的8bit。
  When the row is in the buffer, it can be transferred by successive column addresses at whatever the width of the DRAM is (typically 4, 8, or 16 bits in DDR3).  在上例中，When the row is in the buffer, it can be transferred by successive column addresses at 8bit.
\课-计算机组成\电子书及补充读物\DRAM\DRAM的结构原理剖析-CSDN博客-210525.docx 很有用

## Slide 16
Modern DRAMs are organized in banks, typically four for DDR3.
Sending a PRE (precharge) command opens or closes a bank.
  Memory addr: [bank-addr ] [row-addr] [column-addr],
    E.g. : 24-bit address [2] [11] [11]
  Each bank consists of a series of rows.
A row address is sent with an Act (activate), which causes the row to transfer to a buffer.
When the row is in the buffer, it can be transferred by successive column addresses at whatever the width of the DRAM is (typically 4, 8, or 16 bits in DDR3) or by specifying a block transfer and the starting address.
FIGURE 5.4 Internal organization of a DRAM.
Internal organization of a DRAM

## Slide 17: Advanced DRAM Organization
Bits in a DRAM are organized as a rectangular array
  DRAM accesses an entire row
  Burst mode: supply successive words from a row with reduced latency
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
  Example of Burst mode

## Slide 18: DRAM Generations
Year | Capacity | $/GB
1980 | 64Kbit | $1500000
1983 | 256Kbit | $500000
1985 | 1Mbit | $200000
1989 | 4Mbit | $50000
1992 | 16Mbit | $15000
1996 | 64Mbit | $10000
1998 | 128Mbit | $4000
2000 | 256Mbit | $1000
2004 | 512Mbit | $250
2007 | 1Gbit | $50

## Slide 19: DRAM Performance Factors
Row buffer
  Allows several words to be read and refreshed in parallel
Synchronous DRAM (SDRAM)
  DRAMs added clocks
  Allows for consecutive accesses in bursts without needing to send each address
  Improves bandwidth
DRAM banking
  Allows simultaneous access to multiple DRAMs
  Improves bandwidth

## Slide 20: Increasing Memory Bandwidth
4-word wide memory
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  Bandwidth = 16 bytes / 17 cycles = 0.94 B/cycle
4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 B/cycle
以后再讲

## Slide 21: Flash Storage
Nonvolatile semiconductor storage
  100× – 1000× faster than disk
  Smaller, lower power, more robust
  But more $/GB (between disk and DRAM)

## Slide 22: Flash Types
NOR flash: bit cell like a NOR gate
  Random read/write access
  Used for instruction memory in embedded systems
NAND flash: bit cell like a NAND gate
  Denser (bits/area), but block-at-a-time access
  Cheaper per GB
  Used for USB keys, media storage, …
Flash bits wears out after 1000’s of accesses
  Not suitable for direct RAM or disk replacement
  Wear leveling: remap data to less used blocks

## Slide 23: Disk Storage
Nonvolatile, rotating magnetic storage

## Slide 24: Disk Sectors and Access
Each sector records
  Sector ID
  Data (512 bytes, 4096 bytes proposed)
  Error correcting code (ECC)
    Used to hide defects and recording errors lkj：SSD固态硬盘
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads
  Rotational latency
  Data transfer
  Controller overhead

## Slide 25: Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
Average read time
  4ms seek time
  + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms

## Slide 26: Disk Performance Issues
Manufacturers quote average seek time
  Based on all possible seeks
  Locality and OS scheduling lead to smaller actual average seek times
Smart disk controller allocate physical sectors on disk
  Present logical sector interface to host
  SCSI, ATA, SATA
Disk drives include caches
  Prefetch sectors in anticipation of access
  Avoid seek and rotational delay

## Slide 27: 5.3 Cache Memory
Cache
  Also known as “Cache Memory”, initially all entries are empty.
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches
Figure 5.7 The cache: word Xn is not initially in the cache.
Two issues:
  How do we know if a data item is in the cache?
  If it is, how do we find it?

## Slide 28: Direct Mapped Cache
Where can a block be placed in the upper level (cache)?
Algorithm: Index is the cache block address, it is
  (memory block address) modulo (the number of blocks in the cache)
The cache has 2n blocks, index is equal to the lowest n bits of memory block address. Here n=3.
8 Block of cache
5 bit memory block address
index

## Slide 29: The basics of Cache
For each item of data at the memory, there is exactly one location in the cache where it might be.
  e.g., lots of items at the lower level(memory) share locations in the upper level(cache)

## Slide 30: Tags and Valid Bits
How do we know which particular memory block is stored in a cache location?
  Store memory block address as well as the data
  Actually, only need the high-order bits (tag)
    memory block address = { tag, index}
    e.g. memory block address =10011,tag=10,index=011
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
a. The initial state of the cache after power-on |  |  | 
What if there is no data in a location?
  V (Valid bit): 1 = present, 0 = not present
  Initially all of V are 0

## Slide 31: Accessing a cache---how do we find it?
32-bit or 64-bit memory address
Index=(memory block address) modulo (the number of blocks in the cache)
e.g. 011 = 10011 % 1000 , or 3=19 % 8
Byte offset
Index
TAG
Block address MOD Numbers of Cache Block
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 
a. The initial state of the cache after power-on |  |  | 
V:valid bit

## Slide 32: Access sequence: figure b,c,d,e, f,g,h,i
Mem Block address (red address indicates hit)：
10110,11010,10110,11010, 10000,00011,10000,10010
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
b. After handling a miss of address(10110) |  |  | 
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
c. After handling a miss of address(11010) |  |  | 
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
d. After handling a hit of address(10110) |  |  | 
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
e. After handling a hit of address(11010) |  |  | 

## Slide 33: Access sequence
10110,11010,10110,11010, 10000,00011,10000,10010
Index | V | Tag | Data
000 | Y | (10)2 | Memory(10000)
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
f. After handling a miss of address(10000) |  |  | 
Index | V | Tag | Data
000 | Y | (10)2 | Memory(10000)
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | Y | (00)2 | Memory(00011)
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
g. After handling a miss of address(00011) |  |  | 
Index | V | Tag | Data
000 | Y | (10)2 | Memory(10000)
001 | N |  | 
010 | Y | (11)2 | Memory(11010)
011 | Y | (00)2 | Memory(00011)
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
h. After handling a hit of address(10000) |  |  | 
Index | V | Tag | Data
000 | Y | (10)2 | Memory(10000)
001 | N |  | 
010 | Y | (11)→ (10)2 | Memory(10010)
011 | Y | (00)2 | Memory(00011)
100 | N |  | 
101 | N |  | 
110 | Y | (10)2 | Memory(10110)
111 | N |  | 
i. After handling a miss of address(10010) |  |  | 

## Slide 34: Direct Mapped Cache construction
1 block includes only 1 word (4 byte) here
What kind of locality are we taking advantage of?
temporal
2
Answer for two issues:
  How do we know if a data item is in the cache?
  If it is, how do we find it?
32-bit memory address

## Slide 35: Direct Mapped Cache construction
1 block includes only 1 word (4 byte)
64-bit memory address

## Slide 36: Larger blocks exploit spatial locality
Taking advantage of spatial locality to lower miss rates with many word in the block:
direct-mapped cache

## Slide 37: Example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
  The processor can request both an instruction word and a data word on every clock.
  D-cache: write-through or write-back
SPEC2000 miss rates
  I-cache: 0.4%
  D-cache: 11.4%
  Weighted average: 3.2%

## Slide 38: Example: Intrinsity FastMATH
  16 words per block here vs 4 words per block there

## Slide 39: How many total number of bits needed for a cache in direct-mapped cache?
64-bit address, n bits index, The block size is 2m words (2m+2 bytes)
The cache size is 2n blocks
The data size in a block: 2m words, 2m+2 bytes, 2m+5 bits
  m bits are used for the word within the block, and two bits are used for the byte part of the address
The size of the tag field is 64 − (n + m + 2).
The total bits in a direct-mapped cache is
  2n ×(block size + tag size + valid field size)
  = 2n ×[2m+5 + 64 − (n + m + 2) + 1] = 2n ×[2m+5 + 63 − n − m)]
64-bits address:

## Slide 40: How many total number of bits needed for a cache in direct-mapped cache?
32-bit address, n bits index, The block size is 2m words (2m+2 bytes)
The cache size is 2n blocks
The data size in a block: 2m words, 2m+2 bytes, 2m+5 bits
  m bits are used for the word within the block, and two bits are used for the byte part of the address
The size of the tag field is 32 − (n + m + 2).
The total bits in a direct-mapped cache is
  2n ×(block size + tag size + valid field size)
  = 2n ×[2m+5 + 32 − (n + m + 2) + 1] = 2n ×[2m+5 + 31 − n − m)]
32-bits address:

## Slide 41: Bits in Cache
Example
How many total bits are required for a direct-mapped cache (16KB of data and 4-word blocks)? assuming a 32-bit ( not 64-bit) address.
Answer
One block=4 words = 16 bytes
Number of blocks = 16K ÷ 16 = 210 blocks, index bits n=10
The data size in a block: 22 words, m=2
The size of the tag field: 32 − (n + m + 2) = 18 bits
Data bits of 1 block =4×32=128 bits
The total bits in cache is
  2n ×(block size + tag size + valid field size)
  = 1024×[128 + 18+ 1] = 2n ×[2m+5 + 31 − n − m)] = 147 Kbits
  The total bytes =147/8 KB = 18.4 KB =1.15*16KB
  It is about 1.15 times of the data

## Slide 42: Bits in Cache
Example
How many total bits are required for a direct-mapped cache (16KB of data and 4-word blocks)? assuming a 32-bit ( not 64-bit) address.
Answer
One block=4 words = 16 bytes
Number of blocks = 16K ÷ 16 = 210 blocks, index bits n=10
The data size in a block: 22 words, m=2
The size of the tag field: 32 − (n + m + 2) = 18 bits
Data bits of 1 block =4×32=128 bits
The total bits in cache is
  Total data size + 2n ×(tag size + valid field size)
  = 16K*8 + 1024×[18+ 1] = 128K+19K = 147 Kbits
本PPT页的方法与上页有区别（但篮框内基本相同），是更好的方法

## Slide 43: Mapping an Address to Multiword Cache Block
Example
Consider a cache with 64 blocks and a block size of 16 bytes.
What cache block number does byte address 1200 map to?
Answer： Cache block number =
(memory Block address) modulo (Number of cache blocks)
Where the memory Block address is
So cache block number =75 modulo 64 =11
The start and end byte address of the block where address 1200 is located in:
Byte address
Bytes per block
1200
16
=
= 75
Byte address
Bytes per block
×Byte per block
Byte address
Bytes per block
×Byte per block
+( Byte per block-1)
1200 1215
Here:
Tag
Index
Offset
0
3
4
9
10
63
4 bits
6 bits
54 bits

## Slide 44: Block Size Considerations
Larger blocks with many bytes should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer blocks
    More competition（i.e. more access to the same cache block ）  increased miss rate
Larger miss penalty
  Fetch more bytes from Memory when miss occurs.
  Can override(消除) benefit of reduced miss rate
  Early restart and critical-word-first can help
    early restart: resume execution as soon as the requested word of the block （e.g. the 2# word in 8-word block） is returned, no wait for entire block, only wait for 0#,1# words.
    critical-word-first: Organize the memory, the requested word is transferred first. The remainder is then transferred, starting from the next word after the requested one and wrapping around to the beginning of the block.

## Slide 45
Figure 5.11 Miss rate versus block size. 4 caches: 4K, 16K, 64K, 256K bytes
The miss rate goes up if block size is too large relative to the cache size.
Each line represents a cache of different size： 4K, 16K, 64K, 256K bytes.
following figure data are based on SPEC92.

## Slide 46: Handling Cache reads hit and Miss
Read hits
  this is what we want !
Read misses
  two kinds of misses:
    instruction cache miss
    data cache miss
  2 kinds of caches
  write-back cache: when cache writes hit, cache system only writes data into cache, don't write into memory.
    The latest data is in cache
    Memory data may be obsolete, when a cache block is removed from cache, it should be written back to memory.
  write-through cache: when cache writes hit, cache system write the data into memory, or cache and memory.
    The latest data is in memory.

## Slide 47
Steps of instruction cache read miss operation
  Step-1: for write-back cache, we write the cache block back to memory, this cache block causes read miss.
    For write-through cache, we do nothing in this step.
  Step-2: for instruction cache miss, we stall the CPU, fetch block from memory, deliver to cache, restart CPU read.
    Step-2.1 Send the original PC value (current PC-4) to the memory.
      Reason of current PC-4 : at the end of 1# cycle (IF stage) in pipeline, PC <-- PC+4, at the begin of 2# cycle (ID stage), we fetch memory block, but [current PC] is ([original PC]+4)
    Step-2.2 Instruct main memory to perform a read and wait for the memory to complete its access.
    Step-2.3 Write the cache entry, putting the data from memory in the data portion of the entry, writing the upper bits of the address (from the ALU) into the tag field,and turning the valid bit on.
    Step-2.4. Restart the instruction execution at the first step, which will refetch the instruction again, this time finding it in the cache.

## Slide 48: Handling Cache reads hit and Miss
Steps of data cache read miss operation
  Step-1: the same with instruction cache read miss
  Step-2: for data cache miss, we stall the CPU, fetch block from memory, deliver to cache, restart memory read cycle.
    Step-2.1 Send the word/double-word address from ALU to the memory for memory block read.
    Step-2.2 Instruct main memory to perform a block read and wait for the memory to complete its access.
    Step-2.3 Write the cache entry, putting the data from memory in the data portion of the entry, writing the upper bits of the address (from the ALU) into the tag field, and turning the valid bit on.
    Step-2.4. restart memory pipeline read cycle, which will refetch the data word/double-word again, this time finding it in the cache.

## Slide 49: Handling Cache Writes hit and Miss
Write hits: Difference Strategy for write-back and write-through cache
  Write-back cache (Causing Inconsistent)
    Write the data into only the data cache, Fast
    Write back cache block to memory when the block is replaced.
    A write-back scheme is more complex to implement than write-through.
    write-back Improves performance, especially when processors can generate writes as fast as (or faster than) the writes can be handled by main memory;

## Slide 50
  Write hits: Different Strategy for write-back and write-through cache
  Write-through cache ( Ensuring Consistent)
    Write the data into both the memory and the cache
    Strategy: writes always update both the cache and the memory
    It is slower because of writing memory, solution: using write buffer

## Slide 51
Usual actions for Write misses :
  First read the entire block into cache from memory
    the word (or double words) that SW/SD instruction writes need not be moved into cache because it will be updated immediately.
  Then write a word (for SW instr.) or double word (for SD instr.) into:
    Only cache (for write-back cache)
    Only memory (for write-through with no write allocate )
    both cache and memory (for write-through with write allocate ).
Options of write misses in write-through caches
  Write allocate
    Allocate a cache block , load memory data into cache, then write data in cache
  No write allocate (aka Write around)
    The data is only written to main memory, not written into the cache. Don’t fetch a memory block to cache.
aka: also known as

## Slide 52: Write-through scheme VS write-back scheme
When data is written into the cache (executing a SW(Store Word) or SD instruction), is the data also written to main memory?
  write-through cache
    yes
    Can always discard cached data, the latest data is in memory
    Cache control bit: only a valid bit
    memory always have latest data
    advantage: Read misses don't result in writing memory, memory hierarchy is consistent and it is simple to implement.
  write-back cache
    no
    Can’t just discard cached data, we have to write it back to memory
    Cache control bits: valid and dirty bits
    Less access to memory, since data often overwritten multiple times
    advantage : Writings occur at speed of cache, writing main memory happens less frequently when multiple writing occur to the same block.

## Slide 53: Write stall
Write stall ---When the CPU must wait for writes to complete during write through
Write buffers
  A small cache that can hold a few values waiting to go to main memory.
  To avoid stalling on writes, many CPUs use a write buffer.
    A write buffer includes one or several entries
  This buffer helps when writes are clustered.
  It does not entirely eliminate stalls since it is possible for the buffer to be full if the write burst is larger than the buffer.

## Slide 54: Write buffers
write
buffer
CPU
in out
DRAM
(or lower mem)
Write Buffer

## Slide 55: Cache总结（SW指令）
以cache写hit时采用write back(方案A)和write through（方案B）为中心，分别有2种cache系统：
  系统A： cache写hit时采用write back(方案A)
  系统B： cache写hit时采用write through（方案B）
SW（store word）指令执行时的操作
  系统A-方案A1：cache写hit时，采用write back只写cache （化1个cycle）;
    cache写miss时，依次完成（1）如果cache dirty先把cache的1个block写回内存（可使用write buffer加快速度，估计化1个cycle），如果cache不dirty则不写回内存（不花时间）。（2）把内存的1个block读入cache（可能化100 cycle）；（3） 写1个字到cache（化1个cycle），不写内存;

## Slide 56: Cache总结（SW指令）
SW（store word）指令执行时的操作，SD指令与此类似
  系统B-方案B1： write through with “Write allocate”.
    Cache写hit时，采用write through既写cache又写内存，写内存时使用write buffer加快速度;
    Cache写miss时，采用Write allocate既写cache又写内存，（1）把内存的1个block读入cache （可能化100 cycle） ，原cache内容直接丢弃；（2）同时写1个字到cache （化1个cycle）和内存（最快时化1个cycle） ，写内存时使用write buffer加快速度（但连续多条SW指令可能引起Write Stall--写停顿，下同）;
  系统B-方案B2： write through with “No write allocate” (Write around)
    Cache写hit时，与B1相同: 采用write through既写cache又写内存，写内存时使用write buffer加快速度;
    cache写miss时，采用“No write allocate”，不在cache中分配一个block，不读内存的1个block到cache中 ，不写cache只写内存(写1个字到内存)，写内存时使用write buffer加快速度，最快时化1个cycle ;

## Slide 57: Cache Misses
On cache hit, CPU proceeds normally
On cache miss, do following thing sequentially
  (1). Stall the CPU pipeline
    freezing the contents of the temporary and programmer-visible registers, not saving registers to stack
    waiting for memory
  (2). Fetch block from next level of hierarchy
  (3A). Instruction cache miss: restart instruction fetch
  (3B). Data cache miss: complete data access
  cache miss vs exception(or interrupt)
  the later requires saving all registers to stack.
部分内容是重复的

## Slide 58: Operating on an instruction cache miss
1. Send the original PC ([current PC]-4) value to the memory.
  Reason of [current PC]-4 : at the end of 1# cycle (IF stage) in pipeline, PC <-- PC+4, at the begin of 2# cycle, we fetch memory block, but [current PC] is ([original PC]+4)
2. Instruct main memory to perform a block read and wait for the memory to complete its access.
3. Write the cache entry: putting 1 block of memory data into data portion of the entry, modifying tag field, and setting valid bit to 1.
4. Restart the instruction execution at the first cycle of pipeline: refetching the instruction from cache, this time finding it hit.
部分内容是重复的

## Slide 59: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI =( N+N*10%*100)/N = 1 + 0.1×100 = 11
    Instruction with write miss: 100 cycle (miss penalty) + 1 cycle (hit test) =101 cycle, suppose not reading memory block to cache, also suppose write to memory and cache simultaneously.
Solution: write buffer
  Write buffer holds data waiting to be written to memory
  It Includes 1 or several entries
  After putting data into write buffer, CPU continues subsequent cycle or instruction immediately
    Only stalls on write if write buffer is already full
部分内容是重复的

## Slide 60: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
    A dirty bit is used which is set when the cache block is modified.
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first
a write-back scheme is more complex to implement than write-through.
部分内容是重复的

## Slide 61: Write Allocation (sub-scheme under write-through)
Only 2 cache schemes: write-through and write-back, write allocation is the sub-scheme under write-through.
What should happen on a write miss in write-through scheme?
Alternatives（二选一的方案） for write-through
  Scheme 1: Write allocate
    Allocate a cache block , load memory data into cache, then write data in cache
  Scheme 2: No write allocate (aka Write around)
    A write miss occurs, but not allocating a cache block, not fetching memory block.
    The data is only written to main memory, not written into the cache.
    Reason： programs often write a whole block before reading it (e.g., initialization). 这时把一个block从内存搬到cache是白费力气，因为block内的所有字都是只写不读（至少在初始化后的一段较长时间内不读取）。
部分内容是重复的

## Slide 62: 5.3.3 Elaboration(详述): operation of write-through cache
Suppose write-through cache is used.
Step 1 in write-through cache: we write the data into the cache while reading the tag;
  if the tag mismatches, then a miss occurs.
    the overwriting of the block in the cache is not catastrophic.
      Since memory has the correct value.
    Step 2: usually a memory block will be copied into cache with 10-100 cycle.
    Step 3: write a word or double words into memory (or both memory and cache).
  If the tag matches, i.e. write hits ,write is finished in one cycle
    correct block has been updated, the processor can continue normally, neither step 2 nor step3 is required.

## Slide 63: 5.3.3 Elaboration: operation of write-back cache
Suppose write-back cache is used.
A write-back scheme is more complex to implement than write-through
When write miss occurs
  Step1:write the dirty block back to memory with 10-100 cycle
    If write-back buffer is used, this 10-100 cycle will decrease to minimum of 1 cycle.
    If dirty-bit is 0, step1 do nothing.
  Step 2: a memory block will be copied into cache with 10-100 cycle.
  Step 3: proceed operation when cache write hits.
Overwriting cache block prior to hit tests is not allowed
  This would destroy the cache block (which is not backed up in memory)
  Although this is allowed for a write-through cache

## Slide 64: 5.3.3 Elaboration: operation of write-back cache
When cache write hits, Method 1 : memory-stores may be finished in 2 cycles
  a cycle to check for a hit
  followed by a cycle to actually perform the write
When cache write hits, Method 2 : memory-stores may be finished using 1 normal cache cycle plus 1 unused cache cycle
  A write buffer must be used to hold data
  The processor lookups cache, and places the data into write buffer in 1 normal cache cycle.
    This take only one normal cache cycle based on pipeline.
    Now cache is hit, the new data in buffer are written into cache on the next unused cache cycle.
    Here the new data is word for LW(Load Word), or double word for LD (Load Double-word),
  If the next unused cache cycle is accounted, total 2 cycles are used.

## Slide 65: 5.3.3 Elaboration: write-back caches also uses write buffers
Many write-back caches also include write buffers (here also called write-back buffer )
  to reduce the miss penalty
  when a miss occurs and a modified block is replaces.
    the modified block is moved to a write-back buffer while the requested block is read from memory.
    The cache block in write-back buffer is later written back to memory.

## Slide 66: 5.3.3 Elaboration: write-back caches also uses write buffers
Many write-back caches also include write buffers (here also called write-back buffer )
  to reduce the miss penalty
  when a miss occurs and a modified block is replaces.
    the modified block is moved to a write-back buffer while the requested block is read from memory.
    The cache block in write-back buffer is later written back to memory.
本页与上页内容全同，仅用于格式刷的黑字体模板来源

## Slide 67: 5.4 Measuring and Improving Cache Performance
We use CPU time to measure cache performance.
CPU time= (CPU execution clock cycles + Memory-stall clock cycles) ×Clock cycle time
Memory-stall clock cycles =Read-stall cycles + Write-stall cycles
For Read-stall:
Read-stall cycles = ×Read miss rate ×Read miss penalty
For a write-through plus write buffer scheme:
Write-stall cycles= ×Write miss rate ×Write miss penalty
+ Write buffer stalls
If the “write buffer stalls” are small, we can safely ignore them .
Reads
Program
Writes
Program

## Slide 68: Combine the reads and writes
In most write-through cache organizations, the read and write miss penalties are the same（假定用前面讲的B1方案，不用B2方案）
  the time to fetch the block from memory.
If we neglect the write buffer stalls, we get the following equation:
Memory-stall clock cycles ＝
× Miss rate × Miss penalty
We can also write this as:
Memory-stall clock cycles ＝
The above Instructions is the number of memory access instructions.
Memory accesses
Program
Instructions
Program
Misses
Instructions
×Miss penalty
×

## Slide 69: Calculating cache performance
Assume:
Instruction cache miss rate 2%
  data cache miss rate 4%
  CPI without any memory stalls 2
  miss penalty 100 cycles
  The Load & stores are 36% of instructions
Question: How faster a processor would run with a perfect cache?
Answer: (下面的单位都是cycles)
  Suppose total instruction count is I.
Instruction miss cycles = I×2%×100 =2.00I
Data miss cycles = I×36%×4%×100 =1.44I
Total memory-stall cycles= 2.00I+ 1.44I =3.44 I
CPI with stall = (total cycles for perfect cache + total memory-stalls) / I
= (2*I + 3.44 *I )/ I = 5.44
Total memory-stall cycles / Total cycles = 3.44 I/5.44I= 63%

## Slide 70: How faster a processor for ideal
What happens if the processor is made faster?
Assume CPI reduces from 2 to 1
Total cycles = total cycles for perfect cache + total memory-stalls
=1*I+3.44*I = 4.44I
CPU time with stalls
CPU time with perfect cache
I×CPIstall×Clock cycle
I×CPIperfect×Clock cycle
CPIstall
CPIperfect
5.44
2
=
=
=
CPU time with stalls
CPU time with perfect cache
I * CPIstall
I * CPIperfect
4.44
1
=
=
=4.44
=2.72
3.44
5.44
3.44
4.44
=63% to
=77%
Total memory-stall cycles / Total cycles = 3.44 I/4.44I= 77%
Total memory-stall cycles / Total cycles
from

## Slide 71: Calculating cache performance with Increased Clock Rate
Suppose we increase the performance of the computer in the previous example：doubling CPU clock rate ，while memory access time does not change.
Question : How much faster will the computer be with the faster clock to slow clock?
Answer
Total miss cycles per instruction = (2%×200) + 36%×(4%×200)=6.88
CPI with cache misses = 2 + 6.88 =8.88
Performance with fast clock
Performance with slow clock
Execution time with slow clock
Execution time with fast clock
I×CPIslow clock×Clock cycle
I×CPIfast clock×Clock cycle/2
5.44
8.88×1/2
=
=1.23
=
=
This, the computer with the faster clock is about 1.2 times faster rather than 2 time faster.
I: Instruction Count
本页内容书上无，不讲

## Slide 72: Average Access Time
Hit time is also important for performance
  Increasing the cache size will cause a bigger cache access time.
AMAT(Average Memory Access Time): the average time to access memory considering hit time, miss penalty, and miss rate.
  N memory access
  Total time of memory access: N * hit-time + N * Miss-rate * Miss-penalty
  AMAT = (N * hit-time + N * Miss-rate * Miss-penalty) / N
  = hit-time + Miss-rate * Miss-penalty
  = Time for a hit + Miss rate × Miss penalty
Example: CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 73: 说明：本页PPT从另一角度计算 Average Memory Access time，最终结果（红色的公式） 与上页PPT相同
Average Memory Access time = (total-hit-time + total-miss-time) / I
=[I * hit rate * Cache time + I * miss rate *(Cache time + Miss_penalty) ] / I
= 99% * 5 + (100%-99%) * 45 =5.5ns
150605标注：这里 I=number of total memory access, Miss penalty=40ns，
hit rate=99%, miss rate =1%
发生缺失的单条指令花时间= Cache time +Miss_penalty=5+40=45ns
Average Memory Access time
= [ I * hit rate * Cache time + I * miss rate *(Cache time + Miss_penalty) ] / I
= [ I * (hit rate + miss rate )* Cache time + I * miss rate * Miss_penalty) ] / I
= [ I * Cache time + I * miss rate * Miss_penalty) ] / I
= Cache time + miss rate * Miss_penalty
Note: (hit rate + miss rate ) =100%

## Slide 74
Risc-V 第5版 P394上面的这段文字，红线画出的instruction 是否应写成 access 才正确？

## Slide 75: Performance Summary
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 76: The disadvantage of a direct-mapped cache
If the CPU requires the following memory units sequentially: word 0,word 8 and word 0. Word 0 and word 8 both are mapped to cache block 0, so the third access will be a miss.
But obviously, if one memory block can be placed in any cache block , the miss can be avoided. So, there is possibility that the miss rate can be improved.
0
0
0
0
1
0
0
1
0
1
0
1
0
0
1
0
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
0
0
C
a
c
h
e
M
e
m
o
r
y
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1

## Slide 77
Direct mapped
  Block can only go in one place in the cache
    Memory-block-address MOD Number-of-blocks-in-cache
Fully associative ：Block can go anywhere in cache.
Set associative
  Block can go in one of a set in the cache.
  A set is a group of blocks in the cache.
    Memory-Block-address MOD Number-of-sets-in-the-cache
  If each set has n blocks, the cache is said to be n-way set associative.
Note that direct mapped is the same as 1-way set associative, and fully associative is m-way set-associative (for a cache with m blocks).

## Slide 78: Figure 8-32 Block Placement

## Slide 79: Q2: Block Identification
Every row of cache has an address tag that stores the main memory address of the data stored in the block.
When checking the cache, the processor will compare the requested memory address to the cache tag -- if the two are equal, then there is a cache hit and the data is present in the cache
Often, each cache block also has a valid bit that tells if the contents of the cache block are valid
不讲

## Slide 80: The basics of a set-associative cache Decreasing miss ratio with associativity
A set-associative cache is divided into some sets. A set contains several blocks.
A memory block is mapped to a set in the cache through a mapping algorithm.
  The memory block can be placed in any block in the corresponding set.
The mapping algorithm is:
Set number (Index) =
(Memory block number) modulo (Number of sets in the cache)
If a set has only one block, this set-associative cache is actually a direct-mapped cache.
If a set-associative cache has only one set, this set-associative cache is called a fully-associative cache.

## Slide 81: The Format of the Physical Memory Address
The Index field selects
  The set, in case of a set-associative cache
  The block, in case of a direct-mapped cache
  Has as many bits as log2(#sets) for set-associative caches, or log2(#blocks) for direct-mapped caches
The Byte Offset field selects
  The byte within the block
  Has as many bits as log2(size of block), here the size of block is total bytes in a block.
The Tag is used to find the matching block within the cache
  Has as many bits as Address_size – Index_size – Byte_Offset_Size

## Slide 82: An eight-block cache configured as variety-way

## Slide 83: Set Associative Cache Organization

## Slide 84: Miss rate versus set-associativity
Assume: there are three small caches, each consisting of four one-word blocks.
One cache is direct-mapped,
the second is two-way set associative
and the third is fully associative.
Question: Given the following sequence of block addresses: 0,8,0,6,8, find the number of misses for each cache organization.
Answer: for direct-mapped 5 misses
Memory block | Hit or miss | Contents after each reference |  |  | 
 |  | Set 0 | Set 1 | Set 2 | Set 3
 |  | Block 0 | Block 1 | Block 2 | Block 3
0 | Miss | M[0] |  |  | 
8 | Miss | M[8] |  |  | 
0 | Miss | M[0] |  |  | 
6 | Miss | M[0] |  | M[6] | 
8 | Miss | M[8] |  | M[6] | 

## Slide 85
Second, for the two-way set associative cache. 4 misses
Memory block | Hit or miss | Contents after each reference |  |  | 
 |  | Set 0 |  | Set 1 | 
 |  | Block 0 | Block 1 | Block 2 | Block 3
0 | Miss | M[0] |  |  | 
8 | Miss | M[0] | M[8] |  | 
0 | Hit | M[0] | M[8] |  | 
6 | Miss | M[0] | M[6] |  | 
8 | Miss | M[8] | M[6] |  | 
Memory block | Hit or miss | Contents after each reference |  |  | 
 |  | Only one set |  |  | 
 |  | Block 0 | Block 1 | Block 2 | Block 3
0 | Miss | M[0] |  |  | 
8 | Miss | M[0] | M[8] |  | 
0 | Hit | M[0] | M[8] |  | 
6 | Miss | M[0] | M[8] | M[6] | 
8 | Hit | M[0] | M[8] | M[6] | 
Finally, for the fully associative cache. 3 misses

## Slide 86: How much of a reduction in the miss rate is achieved by associativity?
The data cache miss rates for organization like the Intrinsity FastMATH processor for SPEC2000 benchmarks with associativity varying from one-way to eight-way .
Data cache organization is 64KB data cache and 16-word block
Associativity | Data miss rate
1 | 10.3%
2 | 8.6%
4 | 8.3%
8 | 8.1%

## Slide 87: Size of tags versus set associativity
Assume
  Cache size is 4K Block
  Block size is 4 words
  Physical address is 32bits
Question
Find the total number of set and total number of tag bits for variety associativity
Answer
Offset size (Byte) = 16= 24 4 bits for byte-offset Number of memory block = 232÷24=228 28 bits for memory Block # Number of cache block = 212 12 bits for cache Block #
For direct-mapped
Bits of index = 12 bits
bits of Tag = (28-12) ×4K=16×4K=64 Kbits

## Slide 88
For two-way associative
Number of cache set = 212 ÷ 2= 211
Bits of index =11 bits
Bits of Tag = (28-11) ×4K=17×4K=68 Kbits
For four-way associative
Number of cache set = 212 ÷ 4= 210
Bits of index =10 bits
Bits of Tag = (28-10) ×4K=18×4K=72 Kbits
For full associative
Number of cache set = 1
Bits of index = 0 bits
Bits of Tag = (28-0) ×4K=112 Kbits
 | Direct | 2-way | 4-way | Fully
Index(bit) | 12 | 11 | 10 | 0
Tag(bit) | 16 | 17 | 18 | 28

## Slide 89
In a direct-mapped cache, there is only one block that can be replaced
In set-associative and fully-associative caches, there are N blocks (where N is the degree of associativity
Choosing which block to replace

## Slide 90: Strategy of block Replacement
Several different replacement policies can be used
  Random replacement - randomly pick any block
    Easy to implement in hardware, just requires a random number generator
    Spreads allocation uniformly(均衡地) across cache
    May evict a block that is about to be accessed
  Least-recently used (LRU) - pick the block in the set which was least recently accessed
    Assumed more recently accessed blocks more likely to be referenced again
    This requires extra bits in the cache to keep track of accesses.
  First in,first out(FIFO)-Choose a block from the set which was first came into the cache

## Slide 91: 5.4.3 Choosing which block to replace
In an associative cache, we must decide which block to replace when a miss happens and the corresponding set is full.
The most commonly used scheme is least recently used (LRU), which we used in the previous example. In an LRU scheme, the block replaced is the one that has been unused for the longest time.
For a two-way set associative cache, the LRU can be implemented easily. We could keep a single bit in each set. We set the bit whenever a specific block in the set is referenced, and reset the bit whenever another block is referenced.
As associativity increases, implementing LRU gets harder.

## Slide 92: 5.4.4 Decreasing miss penalty with multilevel caches
Add a second level cache:
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  Part1: With just primary cache, CPI of 1.0 on a 5GHz machine with a 2% miss rate, 100ns DRAM access
  Miss penalty to main memory is
  The CPI with one level of caching
Total CPI = 1.0 + Memory-stall cycles per instruction
    =( 1.0 *I+ 2%*I × 500 ) / I = 1.0 + 2% × 500 = 11.0
  Part2: Adding 2nd level cache with 5ns access time, decreases miss rate to 0.5%（That is，for n instructions( not n memory accesses)，total 0.5%*n access to DRAM， total 2%*n access to the 2nd level cache ）
  Suppose: no double miss (both instruction cache and data cache miss ) occurs during each one-instruction execution.(书上没说，但这条很重要)
100ns
0.2
= 500 clock cycles
5ns
0.2
= 25 clock cycles=Miss penalty of 2nd level cache
本页及后4页PPT来自MIPS教材

## Slide 93
The CPI with Two level of cache with 0.5% miss rate for main memory
Total CPI = 1.0 + Primary stalls per instruction + Secondary stalls per instruction
= 1 + 2% ×25 + 0.5% × 500
= 1.0 + 0. 5 +2.5 = 4.0
The processor with secondary cache is faster, the faster factor(倍数) is
Using multilevel caches:
  try and optimize the hit time on the 1st level cache
  try and optimize the miss rate on the 2nd level cache
11.0
4.0
=2.8

## Slide 94
while L1 cache hit test is operating, we process L1 cache data fetching simultaneously, these 2 operations begin at the same time and cost same time.
L2 cache operates so.
Fig. Total time of an instruction reading memory with both miss of L1 and L2 cache: 526 cycles

## Slide 95: Decreasing miss penalty with multilevel caches
Total N instructions (e.g. N=10000, 4000 memory access instructions, 6000 other instructions such as ADD、SUB、AND、BEQ、J……, total memory access number: 14000(not N) )
  N*98% instructions without any miss penalty, time A=N*98%*H1 cycle
  N*2% instructions with miss of first level cache, time: B+C= N*2%*(H1+H2) + N*0.5% *M2
    N*1.5% access with hit of 2nd level cache, time B=N*1.5% *(H1+H2)
    N*0.5% access with miss of 2nd level cache, Time C= N*0.5% *(H1+H2+M2)
  3 kinds of access time
    H1: 1 cycle, access none of 2nd level cache and DRAM
    H2: 25 cycles to access 2nd level cache
    M2: 500 cycles, miss penalty to access 2nd level cache (i.e. time to access DRAM)
Total time of N instructions: A+B+C
  = N*98%*H1 + N*2%*(H1+H2) + N*0.5% *M2
  = N*H1 + N*2%*H2 + N*0.5% *M2 = N*(1+2%*25+0.5%*500) = 4*N
average CPI=4N/N=4
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  CPI of 1.0 on a 5GHz machine with a 2% miss rate, 100ns DRAM access
  Adding 2nd level cache with 5ns access time decreases miss rate to 0.5%（That is，for n memory access instructions ，total 0.5%*n access to RAM， total 2%*n access to the 2nd level cache ）
Miss penalty to main memory is
Miss penalty to 2nd level cache is

## Slide 96: Decreasing miss penalty with multilevel caches
Total N instructions (e.g. N=10000, 4000 memory access instructions, 6000 other instructions such as ADD、SUB、AND、BEQ、J……, total memory access number: 14000(not N) )
  N*98% accesses without any miss penalty, time A=N*98%*H1 cycle
  N*2% accesses with miss of first level cache, time: B+C= N*2%*(H1+H2) + N*0.5% *M2
    N*1.5% instructions with hit of 2nd level cache, time B=N*1.5% *(H1+H2)
    N*0.5% instructions with miss of 2nd level cache, Time C= N*0.5% *(H1+H2+M2)
  3 kinds of access time
    H1: 1 cycle, hit time to access first level cache
    H2: 25 cycles, hit time to access 2nd level cache
    M2: 500 cycles, miss penalty to access 2nd level cache (time to access DRAM)
Total time of N instructions: A+B+C
  = N*98%*H1 + N*2%*(H1+H2) + N*0.5% *M2
  = N*H1 + N*2%*H2 + N*0.5% *M2 = N*(1+2%*25+0.5%*500) = 4*N
average CPI=4N/N=4
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  CPI of 1.0 on a 5GHz machine with a 2% miss rate, 100ns DRAM access
  Adding 2nd level cache with 5ns access time decreases miss rate to 0.5%（That is，for n memory access instructions ，total 0.5%*n access to RAM， total 2%*n access to the 2nd level cache ）
Miss penalty to main memory is
Miss penalty to 2nd level cache is
本页是一种错误的解题思路，要引起注意

## Slide 97: 5.4.4 Decreasing miss penalty with multilevel caches
Add a second level cache:
  often primary cache is on the same chip as the processor
  use SRAMs to add another cache above primary memory (DRAM)
  miss penalty goes down if data is in 2nd level cache
Example:
  Part1: With just primary cache, CPI of 1.0 on a 4GHz machine with a 2% miss rate, 100ns DRAM access
  Miss penalty to main memory is
  The CPI with one level of caching
Total CPI = 1.0 + Memory-stall cycles per instruction
    =( 1.0 *I+ 2%*I × 400 ) / I = 1.0 + 2% × 400 = 9
  Part2: Adding L-2 cache with 5ns access time, decreases miss rate to 0.5%（That is，for n instructions( not n memory accesses)，total 0.5%*n access to DRAM， total 2%*n access to the 2nd level cache ）
  Suppose: no double miss (both instruction cache and data cache miss ) occurs during each one-instruction execution.(书上没说，但这条很重要)
100ns
0.25
= 400 clock cycles
5ns
0.25
= 20 clock cycles=Miss penalty of 2nd level cache
同RISC-V教材

## Slide 98
The CPI with Two level of cache with 0.5% miss rate for main memory
Total CPI = 1.0 + Primary stalls per instruction + Secondary stalls per instruction
= 1 + 2% ×20 + 0.5% × 400
= 1.0 + 0. 4 +2 = 3.4
The processor with secondary cache is faster, performance ratio is
Using multilevel caches:
  try and optimize the hit time on the 1st level cache
  try and optimize the miss rate on the 2nd level cache
9.0
3.4
=2.6

## Slide 99: Direct-mapped Cache Example (1-word Blocks)
总结和回顾

## Slide 100: Fully-Associative Cache example (1-word Blocks)
Assume cache has 4 blocks
总结和回顾

## Slide 101: 2-Way Set-Associative Cache
Assume cache has 4 blocks and each block is 1 word
2 blocks per set, hence 2 sets per cache
总结和回顾

## Slide 102: Deep concept in Cache
Four Questions for Memory Hierarchy Designers
Caching is a general concept used in processors, operating systems, file systems, and applications.
There are Four Questions for Memory Hierarchy Designers
Q1: Where can a block be placed in the upper level?
(Block placement)
  Fully Associative, Set Associative, Direct Mapped
Q2: How is a block found if it is in the upper level? (Block identification)
  Use Tag
Q3: Which block should be replaced on a miss? (Block replacement)
  Random, LRU,FIFO
Q4: What happens on a write? (Write strategy)
  Write Back or [Write Through (with Write Buffer)]
总结和回顾

## Slide 103: 5.7 Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM （Virtual Memory）“block” is called a page
  VM translation “miss” is called a page fault？？？
§5.7 Virtual Memory

## Slide 104: 5.7 Virtual Memory
Main memory can act as a cache for the secondary storage (disk)
Advantages:
  illusion of having more physical memory
  program relocation
  protection
Virtual addr.
Physical addr.

## Slide 105: Pages: virtual memory blocks
Page faults: the data is not in memory, retrieve it from disk
  huge miss penalty, thus pages should be fairly large (e.g., 4KB)
  reducing page faults is important (LRU is worth the price)
  can handle the faults in software instead of hardware
  using write-through is too expensive so we use write back

## Slide 106: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms

## Slide 107: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE (Page Table Entry) stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 108: Mapping Pages to Storage
valid bit
0: the page is not present in main memory, and a page fault occurs.
1: the page is present in main memory

## Slide 109: 5.7.1 Placing a page and finding it again ----Page Tables
Virtual memory systems use fully associative mapping method

## Slide 110: 5.7.2 Page faults
When the OS creates a process, it usually creates the space on disk for all the pages of a process.
When a page fault occurs, the OS will be given control through exception mechanism.
The OS will find the page in the disk by the page table.
Next, the OS will bring the requested page into main memory. If all the pages in main memory are in use, the OS will use LRU strategy to choose a page to replace
Virtual page

## Slide 111: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written
5.7.4 What about writes?

## Slide 112: 5.7.5 Making Address Translation Fast----TLB
Fast Translation Using a TLB
  TLB (Translation Look aside Buffer)：A cache for address translations
Address translation requires extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB), it make translation faster.
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  TLB Misses could be handled by hardware or software

## Slide 113: 5.7.5 Making Address Translation Fast----TLB

## Slide 114: TLB Misses (virtual page number Not found in TLB)
When TLB Misses, 2 cases
  If page is in memory
    Load the PTE from memory and retry
    Could be handled in hardware
    Or in software
      Raise a special exception
  If page is not in memory (page fault)
    OS handles fetching the page and updating the page table
    Then restart the faulting instruction

## Slide 115: TLB Miss Handler
TLB miss indicates
  Page present in memory, but PTE not in TLB
  Or page not present in memory
TLB Miss Handler in Intrinsity FastMATH do:
  Hardware saves the virtual page number of the reference into a special register
  Generates an exception which handles the miss in software.
  Exception handler do:
    Use virtual page number to find entry in page table
    Copies PTE (page table entry) in memory to TLB, restarts the instruction, get physical address in TLB.
    If the PTE have a valid physical address, that is OK.
    If the PTE does not have a valid physical address, page fault will occur

## Slide 116: Page Fault Handler
Use faulting virtual address to find PTE
Locate page on disk
Choose page to replace
  If dirty, write to disk first
Read page into memory and update page table
Make process runnable again
  Restart from faulting instruction
本页PPT书上好像没有

## Slide 117
the Intrinsity FastMATH Memory Hierarchy

## Slide 118: TLBs and caches using Write Through cache

## Slide 119: TLBs and caches

## Slide 120: TLBs and caches

## Slide 121
Our virtual memory and cache systems work together as a hierarchy:
  data cannot be in the cache unless it is present in main memory.
The OS helps maintain this hierarchy
  flushing the contents of any page from the cache when it migrate that page to secondary memory.

## Slide 122: Possible combinations of Event
Three different types of misses: TLB miss, page Fault, cache miss
  page Fault =【Page table Miss】in following table）

## Slide 123: Modern Systems
Very complicated memory systems:

## Slide 124: Some Issues
Processor speeds continue to increase very fast — much faster than either DRAM or disk access times
Design challenge: dealing with this growing disparity
Trends:
  synchronous SDRAMs (provide a burst of data)
  redesign DRAM chips to provide higher bandwidth or processing
  restructure code to increase locality
  use prefetching (make cache visible to ISA)