## Slide 1: Chapter 4
The Processor

## Slide 2: Computer Organization
Computer
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU
Registers
……

## Slide 3: 4.1 Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two RISC-V implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: ld, sd
  Arithmetic/logical: add, sub, and, or
  Control transfer: beq
§4.1 Introduction
    实验：实现不少于下列指令
    R-Type：add, sub, and, or, xor, slt,srl；
    I-Type： addi, andi, ori, xori, slti, srli,lw;
    S-Type：sw；
    B-Type：beq；
    J-Type： Jal；

## Slide 4: Instruction Execution
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch comparison
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 5: Register Files--Built using D flip-flops
  32 64-bit Registers；
  Input: 2 5-bit register number/ one 5-bit register number and 64-bit data;
  Output: 64-bit data;
  Register write control。
64 bits

## Slide 6: Register File: Read-Output
  Output from the register
5 bits
5 bits
5 bits
64 bits
64 bits
64 bits
Reg. address
Reg. address
Data output

## Slide 7
Description: 32×64bits Register files
Module regs( input clk, rst, RegWrite,
input [4:0] Rs1_addr, Rs2_addr, Wt_addr,
input [63:0] Wt_data,
output [63:0] Rs1_data, Rs2_data
);
reg [63:0] register [1:31]; // r1 - r31
integer i;
assign rdata_A = (Rs1_addr== 0) ? 0 : register[Rs1_addr]; // read
assign rdata_B = (Rs2_addr== 0) ? 0 : register[Rs2_addr]; // read
always @(posedge clk or posedge rst)
begin if (rst==1)
for (i=1; i<32; i=i+1) register[i] <= 0; // reset
else if ((Wt_addr != 0) && (RegWrite == 1))
register[Wt_addr] <= Wt_data; // write
end
endmodule

## Slide 8: CPU Overview
ADD X5, X6, X7 SUB X5, X6, X7
AND X5, X6, X7 OR X5, X6, X7
LD X4, -24(X8)
SD X4,-24(X9)
BEQ X0,X4, exit1

## Slide 9: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 10: Control

## Slide 11: 4.2 Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information
§4.2 Logic Design Conventions

## Slide 12: Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 13: Sequential Elements
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 14: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period
  In this book, we use the rising clock edge to update register. 书P242

## Slide 15: 4.3 Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a RISC-V datapath incrementally
  Refining the overview design

## Slide 16: Instruction Fetch
64-bit register
Increment by 4 for next instruction

## Slide 17: RISC-V fields (format)
opcode：basic operation of the instruction.
rs1： the first register source operand.
rs2： the second register source operand.
rd： the register destination operand.
funct： function,this field selects the specific variant of the operation in the op field.
Immediate: address or immediate

## Slide 18: Instruction execution in RISC-V
Fetch :
  Take instructions from the instruction memory
  Modify PC to point the next instruction
Instruction decoding & Read Operand:
  Will be translated into machine control command
  Reading Register Operands, whether or not to use
Executive Control:
  Control the implementation of the corresponding ALU operation
Memory access:
  Write or Read data from memory
  Only ld/sd
Write results to register:
  If it is R-type instructions, ALU results are written to rd
  If it is I-type instructions, memory data are written to rd
Modify PC for branch instructions

## Slide 19: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 20: Load/Store Instructions
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 21: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value
BEQ X9, X4, exit1

## Slide 22: Branch Instructions
Just re-routes wires
Sign-bit wire replicated
BEQ X9,X4, exit1

## Slide 23: The other elements
Immediate generation unit：
  输入指令产生立即数的逻辑功能
    根据指令类型（加载，存储或者分支指令），产生相应的立即数
  转移指令偏移量左移位的功能
    立即数字段符号扩展为64位结果输出
Immediate generation
  Load:
  0000011
  Store:
  0100011
  Branch:
  1100011
  Jal:
  1101111
S_imm = {{52{inst[31]}}, Inst[31:25], inst[11:7]};
SB_imm = {{51{inst [31]}}, inst[31], inst [7], inst[30:25], inst[11:8],1'b0};
UJ = {{43{inst[31]}}, inst [31], inst[19:12], inst[20], inst[30:21],1'b0};
L_imm = {{52{inst[31]}}, Inst[31:20]};

## Slide 24: Composing the Elements
First-cut（第一茬经历） data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 25: R-Type/Load/Store Datapath

## Slide 26: Full Datapath

## Slide 27: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on opcode
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
上表左边的4bit输入信号：Ainvert, Bnegate, 2位的Operation

## Slide 28
本页PPT的图片来自于附录A

## Slide 29
本页PPT的图片来自于附录A

## Slide 30
本页PPT的图片来自于附录A

## Slide 31
FIGURE 2.18 RISC-V instruction encoding.

## Slide 33: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control

## Slide 34: The Main Control Unit
Control signals derived from instruction

## Slide 35: What should ALU do ?
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on opcode
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
Operation | Function
000 | And
001 | Or
010 | Add
110 | Sub
111 | Slt
opcode | ALUOp | Operation | Funct7 | funct3 | ALU function | ALU control
ld | 00 | load register | XXXXXXX | xxx | add | 0010
sd | 00 | store register | XXXXXXX | xxx | add | 0010
beq | 01 | branch on equal | XXXXXXX | xxx | subtract | 0110
R-type | 10 | add | 0000000 | 000 | add | 0010
 |  | subtract | 0100000 | 000 | subtract | 0110
 |  | AND | 0000000 | 111 | AND | 0000
 |  | OR | 0000000 | 110 | OR | 0001
 |  | SLT | 0000000 | 010 | Slt | 0111

## Slide 36: asserted-assert-deasserted-deassert详解
asserted :有效，逻辑1，即active 状态，如果某引脚是高电平有效，该引脚为asserted指该引脚为高电平；如果某引脚是低电平有效，该引脚为asserted指该引脚为低电平
assert：变有效，变成逻辑1，to become active。如果某引脚是高电平有效，该引脚assert，指该引脚变为高电平；如果某引脚是低电平有效，该引脚assert，指该引脚变为低电平)
Deasserted: 无效，逻辑0，即inactive 状态
deassert：变无效，变成逻辑0，to become inactive。

## Slide 37: Datapath With Control
ADD X5, X6, X7 SUB X5, X6, X7
AND X5, X6, X7 OR X5, X6, X7
LD X4, -24(X8)
SD X4,-24(X9)
BEQ X0,X4, exit1

## Slide 38: R-Type Instruction
ADD X5, X6, X7 SUB X5, X6, X7
AND X5, X6, X7 OR X5, X6, X7

## Slide 39: Load Instruction
LD X4, -24(X8)
SD X4,-24(X9)

## Slide 40: BEQ Instruction
BEQ X0,X4, exit1

## Slide 41: Jal Instruction
jal x1, procedure
imm[20] | imm[10:1] | imm[11] | imm[19:12] | rd | opcode
Write PC+4 to rd
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value and update PC

## Slide 42: Scheme of Controller
2-level decoder
First
Main
decoder
ALU
Decoder
Second
Control Signals (7)
opcode(7)
rd
funct(3)
rs1
rs2
funct(7)
ALU operation(4)
ALU op(2)
Defined
Defined
instruction opcode
(7)

## Slide 43: Signals for datapath Defined 7 control signals
Signal name | Effect when deasserted(=0) | Effect when asserted(=1)
RegWrite | None | Register destination input is written with the value on the Write data input
ALUScr | The second ALU operand come from the second register file output (Read data 2) | The second ALU operand is the sign-extended lower 16 bits of the instruction..
Branch （PCSrc） | The PC is replaced by the output of the adder that computers the value PC+4 | The PC is replaced by the output of the adder that computers the branch target.
Jump | The PC is replaced by PC+4 or branch target | The PC is updated by jump address computed by adder
MemRead | None | Data memory contents designated by the address input are put on the Read data output.
MemWrite | None | Data memory contents designated by the address input are replaced by value on the Write data input.
MemtoReg (2位) | 00：The value fed to register Write data input comes from the Alu | 01：The value fed to the register Write data input comes from the data memory.
 |  | 10：The value fed to the register Write data input comes from PC+4

## Slide 44: Our Simple Control Structure
All of the logic is combinational
We wait for everything to settle down, and the right thing to be done
  ALU might not produce right answer? right away
  we use write signals along with clock to determine when to write
Cycle time determined by length of the longest path
Instruction n
Instruction n+1
控制器
时钟下触发下一条指令
Datapath
Memory
We are ignoring some details like setup and hold times

## Slide 45: Designing the Main Control Unit First level
Main Control Unit function
  ALU op (2)
  Divided 6 control signals into 2 groups
    4 Mux
    3 R/W
control
Instruction opcode (7)
ALU op (2)
Mux (4)
R/W (3)
ALUScr
Branch
MemtoReg Jump
MemRead
MemWrite
RegWrite
ld | 00
sd | 00
Beq | 01
R-type | 10

## Slide 46: Truth Table for Main decoder
jump
Instruction | ALUSrc | MemtoReg | Reg Write | Mem Read | Mem Write | Branch | Jump | ALU Op1 | ALU Op2
R-format |  |  |  |  |  |  |  |  | 
Ld |  |  |  |  |  |  |  |  | 
Sd |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
Jal |  |  |  |  |  |  |  |  | 

## Slide 47: Truth tables & Circuitry of main Controller
输入 |  | 输出 |  |  |  |  |  |  |  | 
Instruction | OPCode | ALUSrcB | Memto-Reg | Reg Write | Mem Read | Mem Write | Branch | Jump | ALUOp1 | ALU Op0
R-format | 0110011 | 0 | 00 | 1 | 0 | 0 | 0 | 0 | 1 | 0
Ld(I-Type) | 0000011 | 1 | 01 | 1 | 1 | 0 | 0 | 0 | 0 | 0
sd(S-Type) | 0100011 | 1 | X | 0 | 0 | 1 | 0 | 0 | 0 | 0
beq(SB-Type) | 1100111 | 0 | X | 0 | 0 | 0 | 1 | 0 | 0 | 1
Jal(UJ-Type) | 1101111 | X | 10 | 1 | 0 | 0 | 0 | 1 | X | X

## Slide 48: Main Controller Code
指令译码器参考描述
`define CPU_ctrl_signals {ALUSrc_B,MemtoReg,RegWR,MemWrite,Branch,Jump,ALUop}
always @* begin
case(OPcode)
5‘b01100: begin CPU_ctrl_signals = ?; end //ALU
5’b00000: begin CPU_ctrl_signals = ?; end //load
5’b01000: begin CPU_ctrl_signals = ?; end //store
5’b11000: begin CPU_ctrl_signals = ?; end //beq
5’b11011: begin CPU_ctrl_signals = ?; end //jump
5’b00100: begin CPU_ctrl_signals = ?; end //ALU(addi;;;;)
……
default: begin CPU_ctrl_signals = ?; end
endcase
end

## Slide 49: Design the ALU Decoder second level
ALU operation is decided by 2-bit ALUOp derived from opcode, and funct7 & funct3 fields of the instruction
  Combinational logic derives ALU control
opcode | ALUOp | Operation | Funct7 | funct3 | ALU function | ALU control
ld | 00 | load register | XXXXXXX | xxx | add | 0010
sd | 00 | store register | XXXXXXX | xxx | add | 0010
beq | 01 | branch on equal | XXXXXXX | xxx | subtract | 0110
R-type | 10 | add | 0000000 | 000 | add | 0010
 |  | subtract | 0100000 | 000 | subtract | 0110
 |  | AND | 0000000 | 111 | AND | 0000
 |  | OR | 0000000 | 110 | OR | 0001
 |  | SLT | 0000000 | 010 | Slt | 0111
4位ALU control的最高位总是0，可以去掉，变成3位ALU control（下页的verilog代码中就只有3位）

## Slide 50: ALU Controller Code
ALU Control HDL Description
assign Fun = {Fun3,Fun7};
always @* begin
case(ALUop)
2’b10: ALU_Control = ? ; //add计算地址
2’b11: ALU_Control = ? ; //sub比较条件
2’b00:
case(Fun)
4'b0000: ALU_Control = 3'b010 ; //add
4’b0001: ALU_Control = ? ; //sub
4’b1110: ALU_Control = ? ; //and
4’b1100: ALU_Control = ? ; //or
4’b0100: ALU_Control = ? ; //slt
4’b1010: ALU_Control = ? ; //srl
4’b1000: ALU_Control = ? ; //xor
……
default: ALU_Control=3'bx;
endcase
2’b01:
case(Fun3)
………………………………………
endcase
4位ALU control的最高位总是0，可以去掉，变成3位ALU control（本页的verilog代码中就只有3位）

## Slide 51: Jal Instruction
jump
jal x1, procedure
imm[20] | imm[10:1] | imm[11] | imm[19:12] | rd | opcode
Write PC+4 to rd
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value and update PC
画了灰色阴影的部件在本指令执行时不起作用，下同
仅当jal指令执行时，控制信号jump=1，其它时候为0
仅当beq指令执行时，控制信号branch=1，其他时候为0

## Slide 52: R-Type Instruction
jump
add x9, x20, x21
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 53: Load Instruction
jump
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Read memory and update register
ld x1, 200(x2)

## Slide 54: Store Instruction
jump
sd x1, 200(x2)
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Write register value to memory

## Slide 55: BEQ Instruction
jump
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value and update PC
beq x1, x2，200
imm[12] | imm[10:5] | rs2 | rs1 | funct3 | imm[4:1] | imm[11] | opcode

## Slide 56: Single Cycle Implementation:performance for ld instruction
Calculate cycle time assuming negligible delays except:
  memory (200ps), ALU and adders (200ps), register file access (100ps)
200ps
200ps
200ps
100+100=200ps
jump

## Slide 57: Performance in Single Cycle Implementation
Let’s see the following table:
The conclusion:
  Different instructions needs different time.
  The clock cycle must meet the need of the slowest instruction. So, some time will be wasted.
Let’s see the following table:
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 58: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Wasteful of area. If the instruction needs to use some functional unit multiple times.
  E.g., the instruction ‘mult’needs to use the ALU repeatedly. So, the CPU will be very large.
  Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 59: Pipelining Analogy
Pipelined laundry: overlapping execution
  The washer, dryer, “folder,” and “storer” ，each take 30 minutes
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/(0.5n + 1.5) ≈ 4 = number of stages

## Slide 60: RISC-V Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 61: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 62: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Tc:每执行一条指令需要的时间

## Slide 63: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 64
We assume the write to the register file occurs in the first half of the clock cycle and the read from the register file occurs in the second half. We use this assumption throughout this chapter.

## Slide 65: Pipelining and ISA Design
RISC-V ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
c.f. 【拉丁语】 confer（比较 compare）

## Slide 66: Hazards (冒险 遇险)
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 67: Structure Hazards
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 68: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add x19, x0, x1 sub x2, x19, x3
Pipeline stall is given the nickname bubble.

## Slide 69: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath
aka: also known as 也称为. 书P271说：The name “forwarding” comes from the idea that the result is passed forward（向将来递交） from an earlier instruction to a later instruction. “Bypassing”（旁路，绕过） comes from passing the result around the register file to the desired unit.

## Slide 70: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
Pipeline stall is given the nickname bubble.

## Slide 71: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
Pipeline stall is given the nickname bubble.

## Slide 72: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for a = b + e; c = b + f;
ld x1, 0(x0)
ld x2, 8(x0)
add x3, x1, x2
sd x3, 24(x0)
ld x4, 16(x0)
add x5, x1, x4
sd x5, 32(x0)
stall
stall
ld x1, 0(x0)
ld x2, 8(x0)
ld x4, 16(x0)
add x3, x1, x2
sd x3, 24(x0)
add x5, x1, x4
sd x5, 32(x0)
11 cycles
13 cycles

## Slide 73: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In RISC-V pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 74: Method 1 of Control Hazards ：Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 75: Method 2 of Control Hazards ： Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  用方法1时，更长的流水线（例如8个stage）往往无法在第2 stage确定是否跳转及下一条要执行指令的地址，例如在第4个stage才能确定，则BEQ指令的第2、3、4 stage都要stall
  Stall penalty becomes unacceptable
Predict outcome of branch（见下页的简单预测方法）
  Only stall if prediction is wrong（实际处理时，BEQ指令下面的那条指令（例如下页图的ld x3 400(x0)）的第1周期操作无效，相当于stall）
In RISC-V pipeline
  Predict branches not taken(预测不跳转)
  Fetch instruction after branch, with no delay

## Slide 76
预测正确时
预测错误时
本图是一种简单粗暴的预测方法：预测不会跳转

## Slide 77: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop，and if-statement branches at loop bottom
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 78: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards (容易遭受hazards)
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture

## Slide 79: Pipeline Summary
For modern pipelines, structural hazards usually revolve（反复出现） around the floating-point unit, which may not be fully pipelined,
control hazards are usually more of a problem in integer programs, which tend to have higher conditional branch frequencies as well as less predictable branches.
Data hazards can be performance bottlenecks in both integer and floating-point programs.
  Often it is easier to deal with data hazards in floating-point programs because the lower conditional branch frequency and more regular memory access patterns allow the compiler to try to schedule instructions to avoid hazards.
书P275的一段话，自看，不讲

## Slide 80: In the next few sections of this chapter, we cover the concept of pipelining using the RISC-V instruction subset (figure 4.12) from the single-cycle implementation in Section 4.4 and show a simplified version of its pipeline.

## Slide 81: RISC-V Pipelined Datapath
§4.6 Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards

## Slide 82: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle
  Each Pipeline register updates at the end of clock cycle
IF-ID reg bits：96 =32+64
ID-EX reg bits：256= 64*4
EX-MEM reg bits：193=64*3+1, zero flag is 1 bit.
MEM-WB reg bits: 128 =64*2
We will expand these register’s length later.

## Slide 83: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle（显示相邻的多条指令在同一个时钟周期的硬件状况，也可看做一条指令在多个周期的硬件状况）
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time （随时间前行的操作图）
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 84: IF for Load, Store, …
Note: PC, register file, both data and instruction memory, every Pipeline register, each has clock pin, but not drawn.

## Slide 85: ID for Load, Store, …

## Slide 86: EX for Load

## Slide 87: MEM for Load

## Slide 88: WB for Load
Wrong register number

## Slide 89: Corrected Datapath for Load

## Slide 90: EX for Store

## Slide 91: MEM for Store

## Slide 92: WB for Store

## Slide 93: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 94: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 95: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 96: Single cycle Datapath With Control
ADD X5, X6, X7 SUB X5, X6, X7
AND X5, X6, X7 OR X5, X6, X7
LD X4, -24(X8)
SD X4,-24(X9)
BEQ X0,X4, exit1

## Slide 97
Control signal for Single cycle CPU
Control signal for pipeline CPU: 3 groups

## Slide 98: Pipelined Control (Simplified)

## Slide 99: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 100: Pipelined Control

## Slide 101: Data Hazards in ALU Instructions
Consider this sequence:
  sub x2, x1,x3 and x12,x2,x5 or x13,x6,x2 add x14,x2,x2 sd x15,100(x2)
We can resolve hazards with forwarding
  How do we detect when to forward?
§4.7 Data Hazards: Forwarding vs. Stalling

## Slide 102: Dependencies & Forwarding

## Slide 103: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs1 = register number for Rs1 sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs1, ID/EX.RegisterRs2
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs1
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRs2
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs1
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRs2
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg

## Slide 104
ld x2, 8(x2)
and x12, x2,x5
当 上面的ld指令与and指令满足1a.条件，会产生严重问题？

## Slide 105: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not x0
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0
  Reason:
    addi x0, x1, 2
    and x12, x0, x5
    or x13, x6, x0

## Slide 106
EX hazard:
  if (EX/MEM.RegWrite
  and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 10
  if (EX/MEM.RegWrite
  and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 10
  MEM hazard:
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01

## Slide 107: Forwarding Paths

## Slide 108: Forwarding Conditions
Mux control | Source | Explanation
ForwardA = 00 | ID/EX | The first ALU operand comes from the register file.
ForwardA = 10 | EX/MEM | The first ALU operand is forwarded from the prior ALU result.
ForwardA = 01 | MEM/WB | The first ALU operand is forwarded from data memory or an earlier ALU result.
ForwardB = 00 | ID/EX | The second ALU operand comes from the register file.
ForwardB = 10 | EX/MEM | The second ALU operand is forwarded from the prior ALU result.
ForwardB = 01 | MEM/WB | The second ALU operand is forwarded from data memory or an earlier ALU result.

## Slide 109: Double Data Hazard
Consider the sequence:
  add x1,x1,x2 add x1,x1,x3 add x1,x1,x4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 110: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd = ID/EX.RegisterRs1))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd = ID/EX.RegisterRs2))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01

## Slide 111
MEM hazard
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd = ID/EX.RegisterRs1))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01

## Slide 112: Datapath with Forwarding

## Slide 113
A MUX (to select the signed immediate as an ALU input) is omitted in previous figures, now added.

## Slide 114
Load-Use Hazard Detection

## Slide 115: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs1, IF/ID.RegisterRs2
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRd = IF/ID.RegisterRs1) or (ID/EX.RegisterRd = IF/ID.RegisterRs2))
If detected, stall and insert bubble

## Slide 116: How to Stall the Pipeline
Let Nop instruction replace [and x4, x2, x5] in previous PPT page to execute in EX, MEM, WB stages, i.e. do nothing in EX, MEM, WB stages
  Nop instruction exists in some computers and do “no operation”.
Force control values in ID/EX register to 0
  In EX, MEM and WB stages instruction [and x4, x2, x5] do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Instruction following LD is fetched again
  1-cycle stall(磨洋工) allows MEM to read data for ld
    Can subsequently forward to EX stage

## Slide 117: Load-Use Data Hazard
Stall inserted here
At end of CC3, PC and IF-ID register are unusually not updated.
and指令被读出并写入IF-ID
or指令被读出但没有写入IF-ID
or指令被再次读出，并写入IF-ID

## Slide 118: Datapath with Hazard Detection
The sign-extended immediate and branch logic are omitted in above figure.
Only when Load-Use Hazard Detection is true, PCWrite, IF/Dwrite, and 8-bit control signals (ALUOP, ALUSrc…from top MUX) are all 0s. In other case, PCWrite, IF/Dwrite are always asserted(=1).

## Slide 119
  Load-Use Hazard
  ld x2, 20(x1)
  and x4, x2, x5
When Load-Use Hazard Detection is true, we must avoid writing register file or memory during EX, MEM, WB stages of above “and x4, x2, x5”
  So 8-bit control signals (ALUOP, ALUSrc…) are written into ID/EX register with all 0s
  More accurately, only the signals RegWrite and MemWrite need be 0, while the other control signals can be don’t cares.

## Slide 120: Stalls and Performance
Stalls（磨洋工） reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture

## Slide 121: Branch Hazards
If branch outcome is to jump to [72 ld x4,100(x7)]
§4.8 Control Hazards
PC
Flush these instructions
(Set control values to 0)

## Slide 122: Reducing Branch Delay
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Example: branch taken
  36: sub x10, x4, x8 40: beq x1, x3, 16 // PC-relative branch // to 40+16*2=72 44: and x12, x2, x5 48: orr x13, x2, x6 52: add x14, x4, x2 56: sub x15, x6, x7 ... 72: ld x4, 50(x7)

## Slide 123: Example: Branch Taken

## Slide 124: Example: Branch Taken

## Slide 125
if an ALU instruction immediately preceding a branch produces the operand for the test in the conditional branch, a stall will be required, since the EX stage for the ALU instruction will occur after the ID cycle of the branch.
By extension, if a load is immediately followed by a conditional branch that depends on the load result, two stall cycles will be needed, as the result from the load appears at the end of the MEM cycle but is needed at the beginning of ID for the branch.

## Slide 126: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add x4, x5, x6
ld x1, addr
beq x1, x4, target

## Slide 127: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
ld x1, addr
beq x1, x0, target

## Slide 128: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from following 4-byte or branch target
    If wrong, flush pipeline and flip prediction

## Slide 129: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on the last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 130: 2-Bit Predictor
Only change prediction on two successive mispredictions
00
01
10
11
Branch is Taken with state change: state number is incremented
Branch is Not taken with state change : state number is decremented

## Slide 131: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch, 性能不如预测不跳转的简单预测系统，本方法无实用价值，无人采用
Branch target buffer （ 0-cycle penalty ）
  Cache of target addresses
  Indexed by PC when instruction fetched
    If cache hits and instruction is branch predicted taken, can fetch target immediately
    BEQ指令的第1 stage (IF)结束时从cache中拿到了跳转目标地址;
    BEQ指令的第2 satge（ID）开始时，跳转地址处的指令开始取出（即开始IF stage）。

## Slide 132: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, syscall, …
Interrupt
  From an external I/O controller, or peripheral devices.
Dealing with them without sacrificing performance is hard.
§4.9 Exceptions

## Slide 133: Exceptions and Interrupts
Many architectures and authors do not distinguish between interrupts and exceptions
i.e. Using either name to refer to both.
  the Intel x86 uses interrupt for both.
  Risc-V use the term exception to refer to both.
    using term interrupt only when the event is externally caused.
§4.9 Exceptions
The only types of exceptions to handle in this chapter
  execution of an undefined instruction
  a hardware malfunction.

## Slide 134: Method 1 in RISC-V: Handling Exceptions
Save PC of offending (or interrupted) instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Save indication of the problem (exception cause )
  In RISC-V: Supervisor Exception Cause Register (SCAUSE)
  64 bits, but most bits unused
    Exception code field: 2 for undefined opcode, 12 for hardware malfunction, …
Jump to handler
  Assume at 0000 0000 1C09 0000hex
  a single entry point for all exceptions
Offending:造成问题的

## Slide 135: Method 2 in other ISA: An Alternate Mechanism: Vectored Interrupts
Vectored Interrupts ( not adopted in RISC-V)
  Handler address determined by the cause
  Interrupt handling entry address, i.e. address of first instruction in interrupt handling program, is called interrupt vector.
Exception vector address to be added to a vector table base register:
  Undefined opcode 00 0100 0000two
  Hardware malfunction: 01 1000 0000two
  …: …
  Suppose: vector table base register=0x80000
    Undefined opcode interrupt entry addr. =0x80000+0x040=0x80040
    Hardware malfunction interrupt entry addr. =0x80000+0x180=0x80180 :
Jump to real handler is possible in interrupt handling program
  e.g. In x86 PC-DOS, int 21H is 0x21# interrupt handling program for system call, it includes many functions such as reading keyboard input, displaying character or string, reading or writing file….., so it includes many real handlers.
00 0100 0000two=0x040
01 1000 0000two=0x180

## Slide 136
Note: X86 PC-DOS belongs to little-endian machine ( upper bytes in upper address)
Vectored Interrupts example in x86 PC-DOS

## Slide 137: Handler (handing program) Actions
Read cause, and transfer to relevant handler
Determine and execute action required, perhaps costing much time.
If restartable
  Take corrective action
  use SEPC to return to program
Otherwise
  Terminate program
    Used for undefined opcode, Hardware malfunction, …
  Report error using SEPC, SCAUSE, …

## Slide 138: Exceptions in a Pipeline
Exception is another form of control hazard
Consider malfunction on add in EX stage
  add x1, x2, x1
  Prevent x1 from being clobbered(影响，破坏)
  Complete previous instructions
  Flush add and subsequent instructions
  Set SEPC and SCAUSE register values
  Transfer control to handler
Similar to mispredicted branch (when branch is predicted not taken)
  Use much of the same hardware

## Slide 139: Pipeline with Exceptions

## Slide 140: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes many instruction for exception, then returns to the aborted instruction that caused exception
    Refetch and execute instruction according to SEPC
PC is saved in SEPC register

## Slide 141: Exception Example
Exception on add in
  40 sub x11, x2, x4 # success 44 and x12, x2, x5 # success 48 or x13, x2, x6 # success 4c add x1, x2, x1 # aborted 50 sub x15, x6, x7 # aborted 54 ld x16, 100(x7) # aborted …
Handler
  1C090000 sd x26, 1000(x10) # success 1c090004 sd x27, 1008(x10) …

## Slide 142: Exception Example
FIGURE 4.64

## Slide 143: Exception Example
FIGURE 4.64

## Slide 144: Multiple Exceptions
Pipelining overlaps multiple instructions
multiple exceptions can occur simultaneously in a single clock cycle, i.e. system could have multiple exceptions at once
  Selecting which exception to handle?
  Solution: to prioritize the exceptions, exception with the highest priority is serviced first.
    SCAUSE reg. records the highest priority exception.
  Simple approach used in RISC-V: deal with exception from earliest instruction. See next page.
    Flush subsequent instructions
    This is the method for “Precise” exception
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order (乱序的) completion （多条指令依次结束的顺序不同于依次开始的顺序）
  Maintaining precise exceptions is difficult!

## Slide 145
Three exceptions(hardware malfunction, wrong memory address, wrong instruction format) occur simultaneously in clock 6, each exception associates an instruction, the earliest instruction (or x13, x2, x6) is selected to handle.
FIGURE 4.64

## Slide 146: Exception Example
FIGURE 4.64

## Slide 147
Precise exceptions: always associating the proper exception with the correct instruction in pipelined computers. e.g. Put 0x4C into SEPC in figure below.
Imprecise exceptions: different from precise one. E.g. PC would normally have 0x58 at the start of clock 7, put 0x58 into SEPC and leave it up to the operating system to determine which instruction caused the problem.
FIGURE 4.64

## Slide 148: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the exception handler program work out questions below
  Which instruction(s) had exceptions
  Which to complete or flush
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines

## Slide 149: Exception and its associated instruction
I/O device requests, hardware malfunctions (such as memory parity check error) are not associated with a specific instruction.
But incorrect op-code exception, exception from non-exist memory address are associated with a specific instruction.
  e.g. LD x26, 0x400(x27) # x27=0x10000 0000 suppose the installed memory is 4G bytes, memory address 0x10000 0400 > 4G, 4G=0x10000 0000

## Slide 150: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice
§4.10 Parallelism via Instructions

## Slide 151: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 152: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated

## Slide 153: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 154: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)

## Slide 155: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 156: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 157: RISC-V with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 158: RISC-V with Static Dual Issue

## Slide 159: Hazards in the Dual-Issue RISC-V
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add x10, x0, x1 ld x2, 0(x10)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 160: Scheduling Example
Schedule this for dual-issue RISC-V
Loop: ld x31,0(x20) // x31=array element add x31,x31,x21 // add scalar in x21 sd x31,0(x20) // store result addi x20,x20,-8 // decrement pointer blt x22,x20,Loop // branch if x22 < x20
 | ALU/branch | Load/store | cycle
Loop: | nop | ld x31,0(x20) | 1
 | addi x20,x20,-8 | nop | 2
 | add x31,x31,x21 | nop | 3
 | blt x22,x20,Loop | sd x31,8(x20) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 161: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name

## Slide 162: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi x20,x20,-32 | ld x28, 0(x20) | 1
 | nop | ld x29, 24(x20) | 2
 | add x28,x28,x21 | ld x30, 16(x20) | 3
 | add x29,x29,x21 | ld x31, 8(x20) | 4
 | add x30,x30,x21 | sd x28, 32(x20) | 5
 | add x31,x31,x21 | sd x29, 24(x20) | 6
 | nop | sd x30, 16(x20) | 7
 | blt x22,x20,Loop | sd x31, 8(x20) | 8

## Slide 163: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 164: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  ld x31,20(x21) add x1,x31,x2 sub x23,x23,x3 andi x5,x23,20
  Can start sub while add is waiting for ld

## Slide 165: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 166: Register Renaming
Reservation stations and reorder buffer effectively provide register renaming
On instruction issue to reservation station
  If operand is available in register file or reorder buffer
    Copied to reservation station
    No longer required in the register; can be overwritten
  If operand is not yet available
    It will be provided to the reservation station by a function unit
    Register update may not be required

## Slide 167: Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  Avoid load and cache miss delay
    Predict the effective address
    Predict loaded value
    Load before completing outstanding stores
    Bypass stored values to load unit
  Don’t commit load until speculation cleared

## Slide 168: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 169: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well
The BIG Picture

## Slide 170: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 171: Cortex A53 and Intel i7
Processor | ARM A53 | Intel Core i7 920
Market | Personal Mobile Device | Server, cloud
Thermal design power | 100 milliWatts (1 core @ 1 GHz) | 130 Watts
Clock rate | 1.5 GHz | 2.66 GHz
Cores/Chip | 4 (configurable) | 4
Floating point? | Yes | Yes
Multiple issue? | Dynamic | Dynamic
Peak instructions/clock cycle | 2 | 4
Pipeline stages | 8 | 14
Pipeline schedule | Static in-order | Dynamic out-of-order with speculation
Branch prediction | Hybrid | 2-level
1st level caches/core | 16-64 KiB I, 16-64 KiB D | 32 KiB I, 32 KiB D
2nd level caches/core | 128-2048 KiB | 256 KiB (per core)
3rd level caches (shared) | (platform dependent) | 2-8 MB
§4.11 Real Stuff: The ARM Cortex-A53 and Intel Core i7 Pipelines

## Slide 172: ARM Cortex-A53 Pipeline

## Slide 173: ARM Cortex-A53 Performance

## Slide 174: Core i7 Pipeline

## Slide 175: Core i7 Performance

## Slide 176: Matrix Multiply
Unrolled C code
1 #include <x86intrin.h>
2 #define UNROLL (4)
3
4 void dgemm (int n, double* A, double* B, double* C)
5 {
6 for ( int i = 0; i < n; i+=UNROLL*4 )
7 for ( int j = 0; j < n; j++ ) {
8 __m256d c[4];
9 for ( int x = 0; x < UNROLL; x++ )
10 c[x] = _mm256_load_pd(C+i+x*4+j*n);
11
12 for( int k = 0; k < n; k++ )
13 {
14 __m256d b = _mm256_broadcast_sd(B+k+j*n);
15 for (int x = 0; x < UNROLL; x++)
16 c[x] = _mm256_add_pd(c[x],
17 _mm256_mul_pd(_mm256_load_pd(A+n*k+x*4+i), b));
18 }
19
20 for ( int x = 0; x < UNROLL; x++ )
21 _mm256_store_pd(C+i+x*4+j*n, c[x]);
22 }
23 }
§4.12 Instruction-Level Parallelism and Matrix Multiply

## Slide 177: Matrix Multiply
Assembly code:
1 vmovapd (%r11),%ymm4 # Load 4 elements of C into %ymm4
2 mov %rbx,%rax # register %rax = %rbx
3 xor %ecx,%ecx # register %ecx = 0
4 vmovapd 0x20(%r11),%ymm3 # Load 4 elements of C into %ymm3
5 vmovapd 0x40(%r11),%ymm2 # Load 4 elements of C into %ymm2
6 vmovapd 0x60(%r11),%ymm1 # Load 4 elements of C into %ymm1
7 vbroadcastsd (%rcx,%r9,1),%ymm0 # Make 4 copies of B element
8 add $0x8,%rcx # register %rcx = %rcx + 8
9 vmulpd (%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
10 vaddpd %ymm5,%ymm4,%ymm4 # Parallel add %ymm5, %ymm4
11 vmulpd 0x20(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
12 vaddpd %ymm5,%ymm3,%ymm3 # Parallel add %ymm5, %ymm3
13 vmulpd 0x40(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
14 vmulpd 0x60(%rax),%ymm0,%ymm0 # Parallel mul %ymm1,4 A elements
15 add %r8,%rax # register %rax = %rax + %r8
16 cmp %r10,%rcx # compare %r8 to %rax
17 vaddpd %ymm5,%ymm2,%ymm2 # Parallel add %ymm5, %ymm2
18 vaddpd %ymm0,%ymm1,%ymm1 # Parallel add %ymm0, %ymm1
19 jne 68 <dgemm+0x68> # jump if not %r8 != %rax
20 add $0x1,%esi # register % esi = % esi + 1
21 vmovapd %ymm4,(%r11) # Store %ymm4 into 4 C elements
22 vmovapd %ymm3,0x20(%r11) # Store %ymm3 into 4 C elements
23 vmovapd %ymm2,0x40(%r11) # Store %ymm2 into 4 C elements
24 vmovapd %ymm1,0x60(%r11) # Store %ymm1 into 4 C elements

## Slide 178: Performance Impact

## Slide 179: Fallacies
Pipelining is easy (!)
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take account of technology trends
    e.g., predicated instructions
§4.14 Fallacies and Pitfalls

## Slide 180: Pitfalls
Poor ISA design can make pipelining harder
  e.g., complex instruction sets (VAX, IA-32)
    Significant overhead to make pipelining work
    IA-32 micro-op approach
  e.g., complex addressing modes
    Register update side effects, memory indirection
  e.g., delayed branches
    Advanced pipelines have long delay slots

## Slide 181: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall
§4.14 Concluding Remarks