## Slide 1
Chapter 1
Introduction

## Slide 2: Uses of Computer Networks
Computer network
  Large number of separate but interconnected computers do a job
  Collection of interconnected, autonomous computing devices
  Interconnected computers can exchange information
Example: the Internet
Network uses
  Access to information
  Person-to-person communication
  Electronic commerce
  Entertainment
  The Internet of Things

## Slide 3: Access to Information (1 of 4)
Web browser and smart phones retrieve information from various Web sites
Social media platforms support targeted behavioral advertising
Online digital libraries and retail sites host digital content
Client-server model forms the basis of network usage
Web applications: Server generates Web pages in response to client requests
Peer-to-peer communication: Individuals form a loose group to communicate with others in the group

## Slide 4: Access to Information (2 of 4)
In the client-server model, a client explicitly requests information from a server that hosts that information.

## Slide 5: Access to Information (3 of 4)
Communication takes the form of the client process sending a message over the network to the server process. The client process then waits for a reply message.

## Slide 6: Access to Information (4 of 4)
In a peer-to-peer system, there are no fixed clients and servers.

## Slide 7: Person-to-Person Communication
Instant messaging
  Allows two people to type messages at each other in real time
Twitter multi-person messaging service
  Allows people to send short messages to their circle of friends or other followers or the whole world
Social network applications
  Information flow driven by the relationships that people declare between each other
Wiki content is a collaborative Web site the members of a community edit

## Slide 8: Electronic Commerce (1 of 2)
Online shopping and financial institution transactions follow client-server model
Online auctions follow peer-to-peer model
  Consumers act as buyers and sellers
  Central server holds the database of products for sale

## Slide 9: Electronic Commerce (2 of 2)
Some forms of e-commerce have acquired little tags based on the fact that ‘‘to’’ and ‘‘2’’ are pronounced the same.

## Slide 10: Entertainment
IPTV (IP Television) systems
  TV shows based on IP technology instead of cable TV or radio transmissions
Media streaming applications
  Internet-provided radio stations, TV shows, and movies
  Content usually moves wirelessly between devices
Game playing using multi-person real-time simulation
Virtual worlds provide a persistent setting
  Thousands of users experience a shared reality with three-dimensional graphics

## Slide 11: The Internet of Things
Ubiquitous computing
  Computing embedded in everyday life
  Home security systems wired with door and window sensors
  Sensors folded into a smart home monitor
  Smart refrigerators
IoT (Internet of Things)
  Sensing and communication take place over the Internet
  Poised to connect every electronic device to the Internet
Power-line networks
  Send information throughout the house over the electric wires

## Slide 12: Types of Computer Networks
Mobile and broadband access networks
  Networks used to access the Internet
Data-center networks
  Networks that house data and applications
Transit networks
  Networks that connect access networks to data centers
Enterprise networks
  Networks used on campuses, in office buildings, or at other organizations

## Slide 13: Broadband Access Networks
Home network use
  Listen to, look at, and create music, photos, and videos
  Access information, communicate with other people, buy products and services
Metcalfe’s law
  Explains how tremendous Internet popularity comes from its size
Broadband access networks
  Delivered to homes using copper, coaxial cable, or optical fiber
  Broadband Internet speeds: gigabit per second to individual homes

## Slide 14: Mobile and Wireless Access Networks (1 of 3)
Wireless hotspots are based on the 802.11 standard
Wireless networking and mobile computing
  Related but not identical
Smartphones combine aspects of mobile phones and mobile computers
Text messaging or texting short message
GPS (Global Positioning System): locates a device
Geo-tagging: annotating photos and videos with the location where they were made

## Slide 15: Mobile and Wireless Access Networks (2 of 3)
Although wireless networking and mobile computing are often related, they are not identical.

## Slide 16: Mobile and Wireless Access Networks (3 of 3)
M-commerce (mobile-commerce) uses mobile phones
NFC (Near Field Communication)
  Allows mobile device to act as an RFID smartcard and interact with a nearby reader for payment
Sensor networks use nodes gathering and relaying information about the physical state of the world
  Nodes may be embedded in familiar devices (cars or phones)
  Nodes may be small, separate devices
  Provide a wealth of data on behavior
  Example: wireless parking meters

## Slide 17: Content Provider Networks
Data-center network
  Internet services are served from ‘‘the cloud’’
  Serves the increasingly growing demands of cloud computing
  Moves large amounts of data between servers in the data center
  Moves data between the data center and the rest of the Internet
Data center network challenges
  Network throughput and energy usage scaling
  ‘‘Cross-section bandwidth”
CDN (Content Delivery Network)
  Large collection of servers, geographically distributed so content is close to the users requesting it

## Slide 18: Transit Networks
Transit network
  Carry traffic between the content provider and the ISP (Internet Service Provider) when they are not directly connected
  Typically charge both the ISP and the content provider for carrying traffic from end-to-end
  Traditionally called backbone networks because they carry traffic between two endpoints
Two trends
  Consolidation of content in a handful of large content providers
  Expansion of the footprint of individual access ISP networks

## Slide 19: Enterprise Networks
Allows resource sharing for devices and information
VPNs (Virtual Private Networks)
  Connect individual networks at different sites into one logical network
  Act as a communication medium among employees
Allows IP telephony or VoIP (Voice over IP)
  Internet technology and computer networks for telephone calls
Allows desktop sharing
  Remote workers can see and interact with a computer screen
Allows electronic business communication

## Slide 20: Personal Area Networks
PANs (Personal Area Networks) let devices communicate over the range of a person. Bluetooth is a short-range wireless network used to connect components without wires.

## Slide 21: Local Area Networks
The configuration on the left represents a wireless 802.11 network. The configuration on the right represents a wired switched Ethernet network.

## Slide 22: Home Networks
Home network LAN
  Broad, diverse range of Internet-connected devices
  Characteristics: manageable, dependable, and secure
Internet of things
  Allows almost any device to connect
Required home network properties
  Easy to install
  Secure and reliable
  Interfaces work between all products
  Reduced consumer device costs

## Slide 23: Metropolitan Area Networks
A MAN (metropolitan area network) where both television signals and the Internet are being fed into the centralized cable head-end (or cable modem termination system) for subsequent distribution to people’s homes.

## Slide 24: Wide Area Networks (1 of 3)
This wide area network illustrates how hosts in Perth, Brisbane, and Melbourne can communicate using leased lines.

## Slide 25: Wide Area Networks (2 of 3)
This wide area network illustrates how hosts in Perth, Brisbane, and Melbourne can communicate via the Internet.
Notes: By using Internet connectivity instead of leasing dedicated transmission lines to connect offices, the wide area network (WAN) connections can be made between the offices as virtual links using the underlying capacity of the Internet.

## Slide 26: Wide Area Networks (3 of 3)
This wide area network illustrates how hosts in Perth, Brisbane, and Melbourne can communicate via an ISP.
Notes: By using a network that is operated by a commercial Internet service provider (ISP), the wide area network (WAN) connections can be made between the offices. This type of set-up may help reduce performance degradation issues that may be seen when connecting over the Internet.

## Slide 27: Internetworks
Internetwork or internet
  A collection of interconnected networks
Network combines subnets and hosts
  Subnet can be described as a ISP network (Figure 1-11)
  Internetwork might be described as a WAN network (Figure 1-9)
An internet
  Interconnection of distinct, independently operated networks
  Connecting a LAN and a WAN or connecting two LANs
  Gateway device makes a connection between two or more networks

## Slide 28: Examples of Networks (1 of 9)
The Internet
  The ARPANET
  NSFNET
  The Internet architecture
Mobile networks
  Mobile network architecture
  Packet switching and circuit switching
  Early generation mobile networks: 1G, 2G, and 3G
  Modern mobile networks: 4G and 5G
Wireless networks (WiFi)

## Slide 29: Examples of Networks (2 of 9)
Figure (a) represents an unsecure network with little redundancy. Figure (b) illustrates a more secure packet-switched network that was initially dismissed as a solution.

## Slide 30: Examples of Networks (3 of 9)
The original ARPANET software was split into two parts: subnet and host. The subnet software consisted of the IMP end of the host-IMP connection, the IMP-IMP protocol, and a source IMP to destination IMP protocol designed to improve reliability.

## Slide 31: Examples of Networks (4 of 9)
Growth of the number of nodes on ARPANET. (a) December 1969. (b) July 1970. (c) March 1971. (d) April 1972. (e) September 1972.

## Slide 32: Examples of Networks (5 of 9)
NSFNET was a backbone network designed to be a successor to the ARPANET that would be open to all university research groups, allowing them to communicate without having to contract with the Department of Defense.

## Slide 33: Examples of Networks (6 of 9)
Cable television infrastructure connects to the Internet
HFC (Hybrid Fiber-Coaxial) network is a single integrated infrastructure
  Uses packet-based transport called DOCSIS (Data Over Cable Service Interface Specification)
DOCSIS transmits a variety of data services, including television channels, high-speed data, and voice
  Device at the home end is called a cable modem
  Device at the cable headend is called the CMTS (Cable Modem Termination System)
  Modem is short for “modulator demodulator”

## Slide 34: Examples of Networks (7 of 9)
A common method for connecting to the Internet from your home is to send
signals over the cable television infrastructure.

## Slide 35: Examples of Networks (8 of 9)
Conventionally, the Internet architecture has been viewed as a hierarchy, with
the tier-1 providers at the top of the hierarchy and other networks further down the
hierarchy, depending on whether they are large regional networks or smaller access
networks.

## Slide 36: Examples of Networks (9 of 9)
Over the past decade, the conventional hierarchy has evolved and ‘‘flattened’’ dramatically.

## Slide 37: Mobile Networks (1 of 6)
The architecture of the mobile phone network has several parts.

## Slide 38: Mobile Networks (2 of 6)
When a user moves out of the range of one cellular base station and into the range of another one, the flow of data must be re-routed from the old to the new cell base station.

## Slide 39: Mobile Networks (3 of 6)
Packet switching comes from the Internet community
  Connectionless networks
  Every packet is routed independently
  If some routers go down during a session, no harm will be done as long as the system can dynamically reconfigure itself
Circuit switching comes from telephone companies
  Connection-oriented networks
  Caller must dial the called party’s number and wait for a connection before talking or sending data
  Route maintained until call is terminated
  Can support quality of service more easily

## Slide 40: Mobile Networks (4 of 6)
First-generation mobile phone systems
  Transmitted voice calls as continuously varying (analog) signals
  AMPS (Advanced Mobile Phone System)
Second-generation (2G) mobile phone systems
  Transmitted voice calls in digital form to increase capacity, improve security, and offer text messaging
  GSM (Global System for Mobile communications)
Third generation (3G) offer digital voice and broadband digital data services
Spectrum scarcity led to today’s cellular network design

## Slide 41: Mobile Networks (5 of 6)
To manage the radio interference between users, the coverage area is divided into cells.

## Slide 42: Mobile Networks (6 of 6)
4G
  Later 4G known as LTE (Long Term Evolution) technology
  Offers faster speeds
  Emerged in the late 2000s
  Quickly became the predominant mode of mobile Internet access in the late 2000s
  Outpacing competitors like 802.16 (WiMiMax)
5G technologies are promising faster speeds
  Up to 10 Gbps
  Set for large-scale deployment in the early 2020s
Main distinction: frequency spectrum they rely on

## Slide 43: Wireless Networks (WiFi) (1 of 6)
IEEE created a wireless LAN standard
  Wireless LAN standard was dubbed 802.11
  Common slang name for it is WiFi
  802.11 systems operate in unlicensed bands
  Example: ISM (Industrial, Scientific, and Medical) bands defined by ITU-R
  802.11 radios compete with cordless phones, garage door openers, and microwave ovens
802.11 network modes: Ad hoc and access point (AP)
Multipath fading causes received signals to fluctuate greatly

## Slide 44: Wireless Networks (WiFi) (2 of 6)
Path diversity overcomes variable wireless conditions
Versions of 802.11
  Original 802.11 ran at either 1 Mbps or 2 Mbps
  802.11b used spread spectrum for rates up to 11 Mbps
  802.11a/g rates were boosted to 54 mbps using OFDM (Orthogonal Frequency Division Multiplexing) modulation
  802.11ac can run at 3.5 Gbps
  802.11ad can run at 7 Gbps (only indoors within a single room)
CSMA (Carrier Sense Multiple Access) scheme
  Handles transmission collision

## Slide 45: Wireless Networks (WiFi) (3 of 6)
802.11 mobility
  Of limited value compared to mobility in mobile phone networks
802.11 security
  WEP (Wired Equivalent Privacy)
  WEP replaced by WiFi Protected Access (initially called WPA)
  WiFi Protected Access (WPA) replaced by WPA2 and 802.1X

## Slide 46: Wireless Networks (WiFi) (4 of 6)
Access points connect to the wired network, and all communication between clients goes through the access point. In an ad hoc network, clients that are in radio range talk directly without an access point.

## Slide 47: Wireless Networks (WiFi) (5 of 6)
At the frequencies used for 802.11, radio signals can be reflected off solid objects so that multiple echoes of a transmission may reach a receiver along different paths. The echoes can cancel or reinforce each other, causing the received signal to fluctuate greatly – a phenomenon known as multipath fading.

## Slide 48: Wireless Networks (WiFi) (6 of 6)
The range of a single radio may not cover the entire system.
Notes: The range of a single radio may not cover the entire system. Computers wait for a short random interval before transmitting and defer their transmissions if they hear that someone else is already transmitting. This scheme makes it less likely that two computers will send at the same time. It does not work as well as in the case of wired networks, though.

## Slide 49: Network Protocols
Design goals
  Reliability (ability to recover from errors, faults, or failures)
  Resource allocation (sharing access to a common, limited resource)
  Evolvability (allowing for incremental deployment of protocol improvements over time)
  Security (defending the network against various types of attacks)
Network protocol design: layering
Connection-oriented vs. connectionless service
Specific service primitives

## Slide 50: Design Goals (1 of 4)
Reliability
  Make a network operate correctly even though it is comprised of a collection of components that are themselves unreliable
    Error detection finds errors in received information
    Error correction corrects a message by recovering the possibly incorrect bits
  Find a working path through a network using routing
    Routing allows network to automatically make the decision

## Slide 51: Design Goals (2 of 4)
Resource allocation
  Scalable designs continue to work well when network gets large
  Statistical multiplexing: sharing based on the statistics of demand
An allocation problem that occurs at every level
  Keeping a fast sender from swamping a slow receiver with data
  Use flow control
Congestion problem
  Occurs when too many computers want to send too much traffic, and the network cannot deliver it all
Quality of service reconciles competing demands

## Slide 52: Design Goals (3 of 4)
Evolvability
  Design issue concerns the evolution of the network
  Over time, networks grow larger and new designs emerge that need to be connected to the existing network
  Use protocol layering structuring mechanism to support change by dividing the overall problem and hiding implementation details
  Use addressing or naming mechanism to identify the senders and receivers involved in a particular message
  Different network technologies often have different limitations
  Overall topic is called internetworking

## Slide 53: Design Goals (4 of 4)
Security
  Confidentiality mechanisms defend against eavesdropping on communications
  Authentication mechanisms prevent someone from impersonating someone else
  Integrity mechanisms prevent surreptitious changes to messages

## Slide 54: Protocol Layering (1 of 4)
Networks organized as a stack of layers or levels
  Each layer built upon the one below it
Communication between corresponding layers
  Use a common protocol referred to as a “layer n protocol”
  Below layer 1 is the physical medium through which actual communication occurs
  Interface lies between each pair of adjacent layers
Network architecture: a set of layers and protocols
Protocol stack: a list of the protocols used by a certain system, one protocol per layer

## Slide 55: Protocol Layering (2 of 4)
A five-layer network where the entities comprising the corresponding layers on different machines are called peers.
Notes: The peers may be software processes, hardware devices, or even human beings. It is the peers that communicate by using the protocol to talk to each other.

## Slide 56: Protocol Layering (3 of 4)
The philosopher-translator-secretary architecture. This figure provides an analogy to explain the idea of multilayer communication.

## Slide 57: Protocol Layering (4 of 4)
An example of information flow supporting virtual communication in layer 5.
Notes: The important thing to understand about Fig. 1-27 is the relation between the virtual and actual communication and the difference between protocols and interfaces.

## Slide 58: Connections and Reliability (1 of 4)
Connection-oriented service
  Modeled after the telephone system
  Service user first establishes a connection, uses the connection, and then releases the connection
  Can conduct a negotiation about the parameters to be used

## Slide 59: Connections and Reliability (2 of 4)
Connectionless service
  Modeled after the postal system
  Packet is a message at the network layer
  Store-and-forward switching: intermediate nodes receive a message in full before sending it on to the next node
  Cut-through switching: transmission of a message at a node starts before it is completely received by the node
  Datagram service: Unreliable (not acknowledged) connectionless service
Reliability characterizes connection-oriented and connectionless services

## Slide 60: Connections and Reliability (3 of 4)
Connection-oriented systems
  Reliable message stream (sequence of pages)
  Reliable byte stream (movie download)
  Unreliable connection (voice over IP)
Connectionless systems
  Reliable message stream (electronic junk mail)
  Reliable byte stream (text messaging)
  Unreliable connection (database query)

## Slide 61: Connections and Reliability (4 of 4)
Six common connection-oriented and connectionless services.

## Slide 62: Service Primitives (1 of 4)
Service
  Formally specified by a set of primitives (operations) available to user processes to access the service
  Primitives tell the service to perform some action or report on an action taken by a peer entity
Six core primitives
  Listen (block waiting for an incoming connection)
  Connect (establish a connection with a waiting peer)
  Accept (accept an incoming connection from a peer)
  Receive (block waiting for an incoming message)
  Send (send a message to the peer)
  Disconnect (terminate a connection)

## Slide 63: Service Primitives (2 of 4)
A minimal example of the service primitives that might provide a reliable byte stream.

## Slide 64: Service Primitives (3 of 4)
Figure 1-30 briefly summarizes how client-server communication might work with acknowledged datagrams so that we can ignore lost packets.

## Slide 65: Service Primitives (4 of 4)
Entities use protocols in order to implement their service definitions.
Notes: A service is a set of primitives (operations) that a layer provides to the layer above it.
A protocol, in contrast, is a set of rules governing the format and meaning of the packets, or messages that are exchanged by the peer entities within a layer.

## Slide 66: Reference Models
The OSI Reference Model
The TCP/IP Reference Model
  The Link Layer
  The Internet Layer
  The Transport Layer
  The Application Layer
A critique of the OSI model and protocols
Critique of the TCP/IP reference model and protocols
The model used in this book

## Slide 67: The OSI Reference Model (1 of 2)
Principles for the seven layers
  Layers created for different abstractions
  Each layer performs well-defined function
  Function of layer chosen with definition of international standard protocols in mind
  Minimize information flow across interfaces between boundaries
  Number of layers should be optimum
Three concepts central to the OSI model:
  Services
  Interfaces
  Protocols

## Slide 68: The OSI Reference Model (2 of 2)
The OSI model has seven layers.

## Slide 69: The TCP/IP Reference Model (1 of 4)
The Link Layer
  Lowest layer in the model
  Describes what links must do to meet the needs of this connectionless internet layer
The Internet Layer
  Permits hosts to inject packets into any network and have them travel independently to the destination
  Defines an official packet format and protocol called IP (Internet Protocol)
  Defines a companion protocol called ICMP (Internet Control Message Protocol) that helps IP function

## Slide 70: The TCP/IP Reference Model (2 of 4)
The Transport Layer
  The layer above the internet layer in the TCP/IP model
  Uses two end-to-end transport protocols
    TCP (Transmission Control Protocol)
    UDP (User Datagram Protocol)
The Application Layer
  Contains all the higher-level protocols

## Slide 71: The TCP/IP Reference Model (3 of 4)
The TCP/IP layers loosely align with the OSI model.

## Slide 72: The TCP/IP Reference Model (4 of 4)
The relation of IP, TCP, and UDP protocols are illustrated. We will study these.

## Slide 73: A Critique of the OSI Model and Protocols (1 of 2)
Bad timing
  Competing TCP/IP protocols were already in widespread use
Bad design
  Both the model and the protocols are flawed
Bad implementations
  Initial implementations were huge, unwieldy, and slow
Bad politics
  Widely thought to be the creature of the European telecommunication ministries, the European Community, and later the U.S. Government

## Slide 74: A Critique of the OSI Model and Protocols (2 of 2)
To prevent bad timing, it is essential that the standards be written in the trough in between the tops of the waves known as the two ‘‘elephants."
Notes: It is essential that the standards be written in the trough in between the two ‘‘elephants.’’ If they are written too early (before the research results are well established), the subject may still be poorly understood; the result is a bad standard. If they are written too late, so many companies may have already made major investments in different ways of doing things that the standards are effectively ignored. If the interval between the two elephants is very short (because everyone is in a hurry to get started), the people developing the standards may get crushed.

## Slide 75: A Critique of the TCP/IP Reference Model and Protocols
Model does not clearly distinguish the concepts of services, interfaces, and protocols
Model is not at all general
  Poorly suited to describing any other protocol stack
The link layer is not really a layer at all in the normal sense of the term
Model does not distinguish between the physical and data link layers
Other protocol implementations were distributed free

## Slide 76: The Model Used in This Book
This model has five layers, running from the physical layer up through the link, network and transport layers to the application layer.

## Slide 77: Standardization
Standardization and open source
Who’s who in the telecommunications world
Who’s who in the international standards world
Who’s who in the Internet standards world

## Slide 78: Standardization and Open Source
Standards define what is needed for interoperability
  No more, no less
WiFi Alliance
  Interoperability within the 802.11 standard
ONF (Open Networking Foundation)
  Interoperability of protocols to control programmable network switches
Two categories of standards
  De facto standards just happened, without any formal plan
  De jure standards are adopted through the rules of some formal standardization body

## Slide 79: Who’s Who in the Telecommunications World
Two extremes
  Small privately owned telephone companies
  National government has a complete legal monopoly on all communication
PTT (Post, Telegraph & Telephone administration)
  Branch of government having telecommunication authority
ITU (International Telecommunication Union)
  United Nations agency
  ITU-T: Telecommunications Standardization Sector

## Slide 80: Who’s Who in the International Standards World (1 of 2)
ISO (International Standards Organization)
  Publishes and produces international standards
NIST (National Institute of Standards and Technology)
  Part of the U.S. Department of Commerce
IEEE (Institute of Electrical and Electronics Engineers)
  The largest professional organization in the world
  IEEE’s 802 committee has standardized many kinds of LANs

## Slide 81: Who’s Who in the International Standards World (2 of 2)
The important ones are marked with *. The ones marked with † gave up and stopped.

## Slide 82: Who’s Who in the Internet Standards World
IAB (Internet Activities Board) oversaw ARPANET
  Renamed Internet Architecture Board
  Communicated with RFCs (Request For Comments)
  IRTF (Internet Research Task Force) subsidiary to IAB
  IETF (Internet Engineering Task Force) subsidiary to IAB
  More formal standardization process was adopted
Internet Society
  Created, populated by people interested in the Internet
World Wide Web Consortium (W3C)
  Develops protocols and guidelines to facilitate long-term growth of the Web

## Slide 83: Policy, Legal, and Social Issues (1 of 3)
Online speech
  Communications Decency Act protects some platforms from federal criminal prosecution
  DMCA takedown notices (after the Digital Millennium Copyright Act) threaten legal action
Net neutrality
  ISPs should provide equal quality of service to a given type of application traffic, regardless of who is sending that content
  No blocking, no throttling, no paid prioritization, transparency
  Does not prevent an ISP from prioritizing any traffic
  Zero rating: ISP might charge its subscribers according to data usage but grant an exemption for a particular service

## Slide 84: Policy, Legal, and Social Issues (2 of 3)
Security
  DDoS (Distributed Denial of Service) attack
  Botnets
  Spam email
  Phishing
Privacy
  Profiling and tracking users by collecting data about their network behavior over time
  Storing cookies in Web browser
  Browser fingerprinting
  Mobile services location privacy

## Slide 85: Policy, Legal, and Social Issues (3 of 3)
Disinformation
  Ill-considered, misleading, or downright wrong information
  Fake news
  Challenges
    How does one define disinformation in the first place?
    Can disinformation be reliably detected?
    What should a network or platform operator do about it once it is detected?

## Slide 86: Metric Units
The principal metric prefixes.