## Slide 1: REVIEW Introduction to computing systems
2020.09.15

## Slide 2: Exam info.
考试时间: 9.18 周五 2:30--5:00
考试地点: 东1A-203/ 东1A-209/东1A-207
闭卷
考试范围：全部
Final score >= 50

## Slide 3: Problem types
Multiple choice 22%
Comprehensive problems 78%
  Data representation 10%
  Gate circuit/truth table 8%
  Read LC3 programs / disassembly 9%
  Implement a new instruction 12%
  LC3 programming 12%
  Interruption 13%
  Read LC3 programs / programming 14%

## Slide 4: Ch1
Why we need a computer?
  Do calculation
  Store information
  Process different types of data
  etc.

## Slide 5: Ch2
How to present data?
  Binary system( bit )
  Unsigned integer
  Signed integer(Complement Representation)
  ASCII code
  Floating-point
  The operation of data

## Slide 6: Ch3
How to implement a computer described before?
n-type/p-type transistor
AND/OR/NOT gate
Decoder
MUX
R-S latch
D-latch
Full Adder
Register
Memory
State machine
Little computer

## Slide 7
Instruction processing
(CH4)
  Fetch
  Decode
  Evaluate Address
  Fetch operands
  Execute operation
  Store result

## Slide 8
Instruction Set Architecture
Machine language(CH5)
LC3
  Memory
  Register
  Opcode
  Data type
  ADD, AND, NOT
  LD, LDI, LDR, ST, STI, STR
  BR, JSR/JSRR, JMP
  TRAP(CH10), RTI
Notes: 需要了解所有指令的功能
指令涉及到的器件
不同指令每个步骤都干了些什么

## Slide 9: Programming in LC3

## Slide 10: Ch7
Assembly language, human-readable
  Opcodes: ADD, AND, LD, ST…….
  Operands: R0-R7, #3, x0F
  Pseudo-operations: .orig .end .blkw .fill .stringz
  Assembly process: two passes
  Symbol table

## Slide 11
I/O
Polling(CH8)
Interrupt-driven(CH10)
stack

## Slide 12: Ch9
How to deal with Input / output ?
System call ---- Trap routine

## Slide 13
We need more powerful programing language
  C, Java, Python…….
  High level abstraction
  Complier translate high level programing language into assembly language
  Fuctions in C language (CH14)
  Pointer and Array in C (CH16)
  Recursion (CH17)
  Data structure (CH19)

## Slide 14: CH1
Transformations Between Layers
Problems
Language
Instruction Set Architecture
Microarchitecture
Circuits
Devices
Algorithms
  stated using "natural language"
  step-by-step procedure, guaranteed to finish
  express the algorithm using C, Java, Python
  the set of instructions, data type
  detailed organization of a processor
Addition, MUX, registers, memory
n-type/p-type MOS Transistor

## Slide 15: CH2 Data and Operation
Computer is a binary digital system
Basic unit of information is the binary digit, or bit.
Values with more than two states require multiple bits.
  A collection of two bits has four possible states: 00, 01, 10, 11
  A collection of three bits has eight possible states: 000, 001, 010, 011, 100, 101, 110, 111
  A collection of n bits has 2n possible states.

## Slide 16: CH2 Data and Operation
Data type: representation and operations within the computer
  Unsigned integer
  Signed intergers
  ASCII
  Floating-point
  String

## Slide 17: CH2 Data and Operation
Unsigned integers
329
102
101
100
101
22
21
20
3x100 + 2x10 + 9x1 = 329
1x4 + 0x2 + 1x1 = 5
most
significant
least
significant

## Slide 18: CH2 Data and Operation
Signed integers
  Two’s Complement Representation
  Sign-extension
  Converting Binary to Decimal
  Converting Decimal to Binary
  Operations: Arithmetic and Logical
  Overflow

## Slide 19: CH2 Data and Operation
  Two’s Complement Representation
Most significent bit is sign bit
510 = 01012
-510 = ?

## Slide 20: CH2 Data and Operation
Sign-extension
510 = 01012 = 000001012
-510 = 10112 = 111110112
00000101 (5)
+ 1011 (-5)
00000000(0)
0101 (5)
+ 1011 (-5)
0000 (0)
1111

## Slide 21: CH2 Data and Operation
  Converting Binary to Decimal
  If leading bit is one, take two’s complement to get a positive number.
  Add powers of 2 that have “1” in the corresponding bit positions.
  If original number was negative, add a minus sign.
X = 01101000two
= 26+25+23
= 64+32+8
= 104ten
X = 11100110two
-X = 00011010
= 24+23+21 = 16+8+2
= 26ten
X = -26ten

## Slide 22: CH2 Data and Operation
Converting Decimal to Binary
  Find magnitude of decimal number. (Always positive.)
  Divide by two – remainder is least significant bit.
  Keep dividing by two until answer is zero, writing remainders from right to left.
  Append a zero as the MS bit; if original number was negative, take two’s complement.
X = 104ten 104/2 = 52 r0 bit 0
52/2 = 26 r0 bit 1
26/2 = 13 r0 bit 2
13/2 = 6 r1 bit 3
6/2 = 3 r0 bit 4
3/2 = 1 r1 bit 5
X = 01101000two 1/2 = 0 r1 bit 6

## Slide 23: CH2 Data and Operation
Operations: Arithmetic and Logical
arithmetic operations
    Addition
    Subtraction
    Sign Extension
  Logical operations
    AND
    OR
    NOT
11 + 01010101 = 11111111
+ 01010101
= 01010100
Truth table

## Slide 24: CH2 Data and Operation
Overflow: If operands are too big, then sum cannot be represented as an n-bit 2’s comp number.
01000 (8) 11000 (-8)
+ 01001 (9) + 10111 (-9)
10001 (-15) 01111 (+15)

## Slide 25: CH2 Data and Operation
Hexadecimal Notation
It is often convenient to write binary (base-2) numbers as hexadecimal (base-16) numbers instead.
011101010001111010011010111
7
D
4
F
8
A
3

## Slide 26: CH2 Data and Operation
Floating point
IEEE 754 Floating-Point Standard (32-bits):
S
Exponent
Fraction
1b
8b
23b
Value = -1.5 x 2(126-127) = -1.5 x 2-1 = -0.75.

## Slide 27: CH2 Data and Operation
n-type MOS Transistor p-type MOS Transistor

## Slide 28: CH3 Digital logic
Inverter (NOT Gate)
In | Out
0 V | 2.9 V
2.9 V | 0 V
In | Out
0 | 1
1 | 0
Truth table

## Slide 29: CH3 Digital logic
OR Gate
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 30: CH3 Digital logic
AND Gate
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 31: CH3 Digital logic

## Slide 32: CH3 Digital logic
Decoder: n inputs, 2n outputs

## Slide 33: CH3 Digital logic
Multiplexer (MUX): n-bit selector and 2n inputs, one output

## Slide 34: CH3 Digital logic
Full Adder: Add two bits and carry-in, produce one-bit sum and carry-out.
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 35: CH3 Digital logic
Four-bit Adder

## Slide 36: CH3 Digital logic
R-S Latch: Simple Storage Element
  R is used to “reset” or “clear” the element – set it to zero.
  S is used to “set” the element – set it to one.
R = S = 1
  hold current value in latch
S = 0, R=1
  set value to 1
R = 0, S = 1
  set value to 0

## Slide 37: CH3 Digital logic
Gated D-Latch
Two inputs: D (data) and WE (write enable)
  when WE = 1, latch is set to value of D
    S = NOT(D), R = D
  when WE = 0, latch holds previous value
    S = R = 1

## Slide 38: CH3 Digital logic
Register

## Slide 39: CH3 Digital logic
Memory: a logical k × m array of stored bits.
•
•
•
k = 2n
locations
m bits
Address Space:
number of locations (usually a power of 2)
Addressability:
number of bits per location (e.g., byte-addressable)

## Slide 40: CH3 Digital logic
address
decoder
word select
word WE
address
write
enable
input bits
output bits
22 x 3 Memory

## Slide 41: CH3 Digital logic
Finite State Machine
State Machine
Combinational
Logic Circuit
Storage
Elements
Inputs
Outputs
Clock
clock circuit triggers transition from one state to the next.

## Slide 42: CH3 Digital logic
Finite State Machine

## Slide 43
LC-3 Data Path
Combinational
Logic
State Machine
Storage

## Slide 44: CH4 Von Newman Model
Von Neuman Model

## Slide 45: CH4 Von Newman Model
How to read/write memory?
What is the function of ALU/PC/IR……
The I/O mechinism?

## Slide 46: CH4 Von Newman Model
Instruction Processing
Decode instruction
Evaluate address
Fetch operands from memory
Execute operation
Store result
Fetch instruction from memory

## Slide 47: CH4 Von Newman Model
What are the functions of each state
  FETCH: Load next instruction
    IR <- mem[PC]
    PC <- PC + 1
  DECODE:
    identify the opcode
    identify other operands from the remaining bit (for LDR, last six bits is offset)

## Slide 48: CH4 Von Newman Model
What are the functions of each state
  Evaluate address
    For instructions that require memory access, compute address used for access(add offset to base register as in LDR)
  Fetch operands
    Obtain source operands needed to perform operation(load data from memory in LDR)

## Slide 49: CH4 Von Newman Model
What are the functions of each state
  Execute
    Perform the operation, using the source operands(send operands to ALU and assert ADD signal)
  Store result
    Write results to destination (register or memory)

## Slide 50: CH5 LC-3
ISA = All of the programmer-visible components and operations of the computer
  memory organization
    address space -- how may locations can be addressed?
    addressibility -- how many bits per location?
  register set
    how many? what size? how are they used?
  instruction set
    Opcodes: ADD, AND, NOT, LD, LDI, LDR, LEA, ST, STR, STI, BR, JSR/JSRR, JMP, RTI, TRAP
    data types
    addressing modes: PC-relative, indirect, base+offset

## Slide 51: CH5 LC-3
NOT R1, R1 ; R1 <- ~R1
AND R1, R1, R2 ; R1 <- R1 and R2
ADD R1, R1, imm ; R1 <- R1 + imm (-24<=imm<=24-1)

## Slide 52: CH5 LC-3
ST R1, PCoffset ;Memory[ PC + Pcoffset] <- R1
STI R1, PCoffset ;Memory[ Memory[ PC + Pcoffset] ]<- R1
STR R1, R2, PCoffset ;Memory[R2 + offset]<- R1

## Slide 53: CH5 LC-3
LEA R1, PCoffset ;R1 <- PC + PCoffset
BRn PCoffset ;if(CC == n) PC <- PC + PCoffset
JMP R1 ;PC <- R1
TRAP x21 ;PC <- Memory[x21]

## Slide 54: CH5 LC-3
JSR PCoffset11 ;R7 <- PC, PC <- PC + PCoffset
JSR R1 ;R7 <- PC, PC <- R1
RTI ;return from interrupt, pop PC, pop PSR, set stack pointer

## Slide 55: CH5 LC-3
The function of all the elements in the data-path ?
Identify all the elements in the data-path to process an instruction of the LC3
How many times does an instruction(for example LDR) access the memory?

## Slide 57: CH7 Assembly Language
Assembly language
  Computers like ones and zeros…
  Humans like symbols…
0001110010000110
ADD R6,R2,R6 ; increment index reg.

## Slide 58: CH7 Assembly Language
Opcodes
  ADD, AND, LD, ST…….
Operands
  Registers: R0 – R7
  Immediate numbers: x0F, #15
  Label: symbolic name of memory location

## Slide 59: CH7 Assembly Language
Label
  assigns a symbolic name to the address corresponding to line
  LOOP ADD R1, R1, #-1
  BRp LOOP
Comment
  anything after a semicolon is a comment

## Slide 60: CH7 Assembly Language
Pseudo-operations
  do not refer to operations executed by program
  used by assembler
Opcode | Operand | Meaning
.ORIG | address | starting address of program
.END |  | end of program
.BLKW | n | allocate n words of storage
.FILL | n | allocate one word, initialize with value n
.STRINGZ | n-character string | allocate n+1 locations, initialize w/characters and null terminator

## Slide 61: CH7 Assembly Language
What is the content of R0 after the following instruction?
.ORIG x3000
AND R0, R0, 0
.fill x1021
ADD R0, R0, 1
.END
1000 000 000 1 00001
Notes: 0001 0000 0010 0001
Add r0, r0, 1

## Slide 62: CH7 Assembly Language
Assembly Process
  Convert assembly language file into an executable file
First Pass:
  scan program file
  find all labels and calculate the corresponding addresses; this is called the symbol table
Second Pass:
  convert instructions to machine language, using information from symbol table

## Slide 63: CH7 Assembly Language
Translate following assembly program
.ORIG x3000
Begin AND R1, R1, 0
ADD R1, R1, #10
Loop LEA R0, Hello
TRAP x22
ADD R1, R1, #-1
BRzp Loop
TRAP x25
Hello .stringz "hello\n"
.end

## Slide 64: CH7 Assembly Language
Translate following assembly program
  First Pass: build the symbol table
.ORIG x3000
Begin AND R1, R1, 0
ADD R1, R1, #10
Loop LEA R0, Hello
TRAP x22
ADD R1, R1, #-1
BRzp Loop
TRAP x25
Hello .stringz "hello\n"
.end
Symbol | Address
Begin | X3000
Loop | X3002
Hello | X3007

## Slide 65: CH7 Assembly Language
Translate following assembly program
  Second Pass: translate into machine language
.ORIG x3000
Begin AND R1, R1, 0
ADD R1, R1, #10
Loop LEA R0, Hello
TRAP x22
ADD R1, R1, #-1
BRzp Loop
TRAP x25
Hello .stringz "hello\n"
.end
Symbol | Address
Begin | X3000
Loop | X3002
Hello | X3007
0011000000000000
0101 001 001 1 00000
0001 001 001 1 01010
1110 000 000000100
1111 0000 00100010
0001 001 001 1 11111
0000 011 111111100
1111 0000 00100101
0000000001101000
0000000001100101
0000000001101100
0000000001101100
0000000001101111
0000000000001010
0000000000000000

## Slide 66: CH8 I/O
Memory-mapped I/O
Polling: CPU keeps checking status register
Interrupts: Device sends a special signal to CPU
POLL LDI R1, DSR BRzp POLL STI R0, DDR
……
DSR .FILL xFE04 DDR .FILL xFE06

## Slide 67: CH8 I/O
Memory-mapped I/O
Location | I/O Register | Function
xFE00 | Keyboard Status Reg (KBSR) | Bit [15] is one when keyboard has received a new character. Bit[14] is one when interrupt is enabled
xFE02 | Keyboard Data Reg (KBDR) | Bits [7:0] contain the last character typed on keyboard.
xFE04 | Display Status Register (DSR) | Bit [15] is one when device ready to display another char on screen.
xFE06 | Display Data Register (DDR) | Character written to bits [7:0] will be displayed on screen.

## Slide 68: CH8 I/O
Implementation

## Slide 69: CH9 TRAP
System call：TRAP
  1. User program invokes system call.
  2. Operating system code performs operation.
  3. Returns control to user program.
vector | symbol | routine
x20 | GETC | read a single character (no echo)
x21 | OUT | output a character to the monitor
x22 | PUTS | write a string to the console
x23 | IN | print prompt to console, read and echo character from keyboard
x25 | HALT | halt the program

## Slide 70: CH9 TRAP

## Slide 71: CH9 TRAP
Write a trap routine
  Memory[TrapVector]
  Must save the value of registers
  Caller save: Save registers destroyed by own instructions or by called routines (if known), if values needed later
    save R7 before TRAP
    save R0 before TRAP x23 (input character)
  Callee save:
    Before start, save any registers that will be altered
    Before return, restore those same registers

## Slide 72: CH9 TRAP
Subroutine
  JSR JSRR
  RET or JMP R7
  How to pass arguments
  How to get return values
  Save registers: caller callee
  Save R7 when call any other subroutine or TRAP

## Slide 73: CH10 Stack and Interrupt
Abstract data type
  Stack: LIFO(last-in first-out), push pop
  Queue: FIFO(First-in first-out), rear front
  Tree

## Slide 74: CH10 Stack and Interrupt
Basic push and pop code
Push
ADD R6, R6, #-1 ; decrement stack ptr STR R0, R6, #0 ; store data (R0)
Pop
LDR R0, R6, #0 ; load data from TOS ADD R6, R6, #1 ; decrement stack ptr
Pop with underflow detection
Push with overflow detection

## Slide 75: CH10 Stack and Interrupt
Implement Interrupt-Driven I/O with stack
  What is PSR?
  Overall mechanism of interrupt
  What information need to store ?
  Transform between supervisor stack and user stack

## Slide 76: CH10 Stack and Interrupt
Implement Interrupt-Driven I/O with stack
  What is PSR?
Processor Status Register
  Privilege [15], Priority Level [10:8], Condition Codes [2:0]

## Slide 77: CH10 Stack and Interrupt
Implement Interrupt-Driven I/O with stack
  What information need to store ?
    PSR (store in supervisor stack)
    PC (store in supervisor stack)
    Register(interrupt routine should save the registers it alters)

## Slide 78: CH10 Stack and Interrupt
Overall mechanism of interrupt
If Priv = 1 (user), Saved.USP = R6, then R6 = Saved.SSP.
Push PSR and PC to Supervisor Stack.
Set PSR[15] = 0 (supervisor mode).
Set PSR[10:8] = priority of interrupt being serviced.
Set PSR[2:0] = 0.
Set MAR = x01IV, where IV = 8-bit interrupt vector provided by interrupting device (e.g., keyboard = x80).
Load memory location (M[x01IV]) into MDR.
Set PC = MDR; now first instruction of ISR will be fetched.

## Slide 79: CH10 Stack and Interrupt
Overall mechanism of interrupt
9. store registers
10. perform the interrupt routine
11. resume registers
12. RTI return
    Pop PC from supervisor stack. (PC = M[R6]; R6 = R6 + 1)
    Pop PSR from supervisor stack. (PSR = M[R6]; R6 = R6 + 1)
    If PSR[15] = 1, R6 = Saved.USP

## Slide 80: CH14 Function
Function definition
Declaration
Run-time stack
What is activation Record ?

## Slide 81: CH14 Function
int NoName(int a, int b) { int w, x, y; . . . return y; }
y
x
w
dynamic link
return address
return value
a
b
bookkeeping
locals
args
R5

## Slide 82: CH14 Function
Activation record
  Return value
    space for value returned by function
    allocated even if function does not return a value
  Return address
    Save pointer to next instruction in calling function
  Dynamic link
    Caller’s frame pointer

## Slide 83: CH14 Function
LC-3 Function Call Implementation
Caller pushes arguments (last to first).
Caller invokes subroutine (JSR).
Callee allocates return value, pushes R7 and R5.
Callee allocates space for local variables.
Callee executes function code.
Callee stores result into return value slot.
Callee pops local vars, pops R5, pops R7.
Callee returns (JMP R7).
Caller loads return value and pops arguments.
Caller resumes computation…

## Slide 84: CH14 Function
Example Function Call
int Volta(int q, int r) { int k; int m; ... return k; } int Watt(int a) { int w; ... w = Volta(w,10); ... return w; }

## Slide 85: Calling the Function
w = Volta(w, 10);
; push second arg AND R0, R0, #0 ADD R0, R0, #10 ADD R6, R6, #-1 STR R0, R6, #0 ; push first argument LDR R0, R5, #0 ADD R6, R6, #-1 STR R0, R6, #0 ; call subroutine JSR Volta
q
r
w
dyn link
ret addr
ret val
a
25
10
25
xFD00
new R6
Note: Caller needs to know number and type of arguments, doesn't know about local variables.
R5
R6

## Slide 86: Starting the Callee Function
; leave space for return value ADD R6, R6, #-1 ; push return address ADD R6, R6, #-1 STR R7, R6, #0 ; push dyn link (caller’s frame ptr) ADD R6, R6, #-1 STR R5, R6, #0 ; set new frame pointer ADD R5, R6, #-1 ; allocate space for locals ADD R6, R6, #-2
m
k
dyn link
ret addr
ret val
q
r
w
dyn link
ret addr
ret val
a
xFCFB
x3100
25
10
25
xFD00
new R6
new R5
R6
R5

## Slide 87: Ending the Callee Function
return k;
; copy k into return value LDR R0, R5, #0 STR R0, R5, #3 ; pop local variables ADD R6, R5, #1 ; pop dynamic link (into R5) LDR R5, R6, #0 ADD R6, R6, #1 ; pop return addr (into R7) LDR R7, R6, #0 ADD R6, R6, #1 ; return control to caller RET
m
k
dyn link
ret addr
ret val
q
r
w
dyn link
ret addr
ret val
a
-43
217
xFCFB
x3100
217
25
10
25
xFD00
R6
R5
new R6
new R5

## Slide 88: Resuming the Caller Function
w = Volta(w,10);
JSR Volta ; load return value (top of stack) LDR R0, R6, #0 ; perform assignment STR R0, R5, #0 ; pop return value ADD R6, R6, #1 ; pop arguments ADD R6, R6, #2
ret val
q
r
w
dyn link
ret addr
ret val
a
217
25
10
217
xFD00
R6
R5
new R6

## Slide 89: CH16 Pointers and Arrays
Pointer
  Address of a variable in memory
  Allows us to indirectly access variables
    in other words, we can talk about its address rather than its value
Array
  A list of values arranged sequentially in memory
  Example: a list of telephone numbers
  Expression a[4] refers to the 5th element of the array a

## Slide 90
Pointer
C language
int i;
int *ptr;
i = 4;
ptr = &i;
*ptr = *ptr + 1;
LC3
; i = 4;
AND R0, R0, #0 ; clear R0 ADD R0, R0, #4 ; put 4 in R0 STR R0, R5, #0 ; store in I
; ptr = &i; ADD R0, R5, #0 ; R0 = addr of i STR R0, R5, #-1 ; store in ptr
; *ptr = *ptr + 1; LDR R0, R5, #-1 ; R0 = ptr LDR R1, R0, #0 ; load *ptr ADD R1, R1, #1 ; add one STR R1, R0, #0 ; store result
ptr=&i=R5
i = 4
dynamic link
return address
return value
R5

## Slide 91: CH16 Pointers and Arrays
Array
C language
int grid[10];
int x;
x = grid[3] + 1
grid[6] = 5;
LC3
; x = grid[3] + 1
ADD R0, R5, #-9 LDR R1, R0, #3 ADD R1, R1, #1
STR R1, R5, #-10
; grid[6] = 5; AND R0, R0, #0 ADD R0, R0, #5
ADD R1, R5, #-9 STR R0, R1, #6
x
grid[0]
grid[1]
grid[2]
grid[3]
grid[4]
grid[5]
grid[6]
grid[7]
grid[8]
grid[9]
R5

## Slide 92: CH17 Recursion
A recursive function is one that solves its task by calling itself on smaller pieces of data.
Recursive Function:
int RunningSum(int n) { if (n == 1) return 1; else return n + RunningSum(n-1); }

## Slide 93: CH17 Recursion
Binary Search
FindExam(studentName, start, end) { halfwayPoint = (end + start)/2; if (end < start) ExamNotFound(); /* exam not in stack */ else if (studentName == NameOfExam(halfwayPoint)) ExamFound(halfwayPoint); /* found exam! */ else if (studentName < NameOfExam(halfwayPoint)) /* search lower half */ FindExam(studentName, start, halfwayPoint - 1); else /* search upper half */ FindExam(studentName, halfwayPoint + 1, end); }

## Slide 94: CH19 Data structures
A data structure is a particular organization of data in memory
  Array
  Struct
  Linked list
  Stack
  Queue
  Tree

## Slide 95: CH19 Data structures
//define a struct
struct flightType { char flightNum[7];
int altitude;
int longitude;
int latitude;
int headin;
double airSpeed;
};
int x;
Struct flightType plane;
int y;
y
plane.flightNum[0]
plane.flightNum[6]
plane.altitude
plane.longitude
plane.latitude
plane.heading
plane.airspeed
x
R5